Summary Table of the comments received during the Public Consultation of the draft amended ERC Decision (98)22

“Exemption from individual licensing of DECT equipment” and the resolution agreed by ECC PT1

| Comment number | Section number/ Clause | Paragraph Figure/ Table | Type of comment (General/ Technical/Editorial) | COMMENTS | Proposed change | Resolution analysis |
| --- | --- | --- | --- | --- | --- | --- |
| AUT_D_SUI/1 | Considering l) |  | General | It is proposed to add a new considering l) in order to reflect the ongoing discussions on the 2 GHz TDD bands in CEPT. | l) that the outcome of the on-going studies regarding the frequency band 1900-1920 MHz could require a revision of this ERC Decision in the near future; | Accepted |
| AUT_D_SUI/2 | DECISES 1.a. |  | Editorial | The current wording of Decides 1.a. is unclear as it mentions both “total radiated power” and “nominal transmit power” for the power limit of 250 mW and these two terms have different meanings. As the radiated power already includes the antenna gain, which is covered in Decides 1.b. the term “nominal transmit power” should be used in Decides 1.a. | nominal transmit power of up to 250 mW (24 dBm) | Accepted |
| NL/1 | Considerings | i) | General | See introductory text | Reference to the CEPT Reports 39 and 41 should be replaced with references to ERC Reports 10, 31 and 100. | Updated version of this comment (see ECC PT1(13)INFO 09) accepted |
| NL/2 | DECIDES | 1 | Technical | See introductory text | TRP should be removed from DECIDES 1a and replaced with a single maximum ERP or e.i.r.p. value. Remove antennagain restriction from DECIDES 1b. | Updated version of this comment (see ECC PT1(13)INFO 09) accepted |
| ASCOM/1 | DECIDES | 1b | Technical | ASCOM has since many years been a leading worldwide supplier of enterprise DECT systems. This include mission critical applications like alert team calls and supervision for hospitals and production lines in factories. The previous version of ERC Decision(98)22 refers to the harmonized standard, which specify 250 mW transmit power and up to 12 dBi antenna gain. The new version of ERC Decision(98)22 has the same total power, but differentiates between omni-directional and directional antennas, allowing 2 and 6 dBi gain respectively. Such a differentiation may have its merits, especially for external antennas, where the definition is obvious. 1) However, what about the common small integrated antennas? See the figure below showing the coverage area for a typical antenna of one of our handsets. It seems to be both omni and directive. However, measurements are made related to the peak. Thus it is clearly more directive than omni. Small integrated antennas always have some losses and have an irregular shape, often a distinctive directivity, due to the large LCD display and/or due to the intended design to direct the power out from the head. It is therefore proposed that integrated antennas are defined as a new category of antennas with a dBi similar to directive antennas. The attached protocol from NEMKO measured on our handsets, show dBi values of 4.9 and 3.4 dBi for integrated antennas. 2) A secondary issue is that commercial external antennas below 8 dBi are hard to find. It is proposed that the limit for directional antennas be raised to 8 dBi, in line with study results PT1 Correspondence Group. The gain for integrated antennas should be at least 4 dBi. | Change DECIDES 1b to the following: b. for external antennas an antenna gain up to 2 dBi for omni-directional antennas and up to 8 dBi for directional antennas, and for integrated antennas an antenna gain of up to 4 dBi. | Addition of a separate case for integrated antennas not accepted as this case is already covered by the two existing (generic) cases. Increase of antenna gain to 8 dBi not accepted as the compromise reached in previous discussions was for 250 mW plus 6 dBi However, the use of an 8 dBi antenna would be possible when the transmit power is reduced correspondingly (from 24 dBm to 22 dBm). |
| DECT Forum/1 | Considering | i) | Technical / Editorial | CEPT Reports 039 and 041 only contain new calculations on interference to DECT. ETSI has during the course of the DECT antenna study period provided the TR 103 089, which contains updated radio parameters also for interference from DECT to UMTS/LTE, which have been used during the study. This TR also gives a detailed description of the different intended DECT system architectures and antenna properties/applications, which were used as background information during the review process. It is felt proper and useful to add ETSI TR 103 089 as a background reference. It may also be of help at future revisions. | Add to paragraph i): and ETSI has provided a comprehensive overview of considered DECT radio properties and intended applications in ETSI TR 103 089. | Accepted |
| DECT Forum/2 | Considering | k) | Technical / Editorial | DECT two main categories, residential and multi-cell enterprise systems, are used both indoors (mainly) and outdoors. All DECT systems are wireless access systems. May be that the term wireless access systems was meant for public access systems ? The Harmonized Standard relates to the terminal directive. Therefore terminals of public DECT systems are covered. Also machine to machine (M2M) communication is an increasingly important DECT application and has thus been added. | Change paragraph k) to: that the Harmonised Standard EN 301 406 contains technical requirements for DECT systems in the frequency band 1880-1900 MHz, covering equipment for home/indoor systems as well as for wireless access systems residential and enterprise systems, for machine to machine communications, as well as for terminals of public access systems; | Accepted |
| DECT Forum/3 | Considering | k) | Technical / Editorial | To further clarify the intended use for the licence exempt DECT systems. The technical discussions have been based on the common understanding that base stations for outdoor coverage extension are intended to be installed below roof top. It is thought to be useful for future revisions to have this information added in the considerings. | Add to the changed paragraph k) or in a new paragraph: Residential and enterprise systems are mainly installed indoors. Base stations for coverage of onsite related outdoor areas, are intended to be installed below rooftop and below 7 m. | Accepted, but replacing system by equipment |
| DECT Forum/4 | DECIDES | 1 | Technical | See the proposed change of adding a new condition c. The antenna gain requirement in EN 301 406 has this construction. This new condition c does not increase the intended maximum eirp limit (but converts a dBi limit to a fixed eirp limit, independent of the actual transmit power). Condition c is an essential extra condition, to be able to compensate for pattern irregularities of small integrated antennas (see below), as well to utilise standard external directive antennas, and also to allow for higher antenna (11-12 dBi) gain to reduce time disperson when required. | Add a new condition c: c. if the power in condition a. is X dB below 24 dBm, then the dBi limits in condition b. are increased by X dB. | Principle accepted, but specifying the EIRP limit instead of the antenna gain |
| DECT Forum/5 | DECIDES | 1b | Technical | External antennas are easy to define as omni or directive, but typical DECT integrated antennas are not as easy. Most DECT antennas are small integrated antennas. Those are a mixture between omni and directional patterns, normally with a distinct directive peak. See attached figure below. The studies at WGSE and PT1 show that interference probability basically relates to the total coverage area and not to the peak. Measutements are related to the peak. Thus the antenna diagram below is clearly more directive than omni. The attached NEMCO measurement report from ASCOM handsets show dBi values of 4,9 and 3,4. However, to clarify the situation, it is proposed to separate the specification between integrated antennas and external antennas. 4 dBi (average between omni and directive) is proposed for integrated antennas. See attached technical information below : « Integrated DECT antennas ». | Change condition b: b. for integrated antennas an antenna gain of up to 4 dBi, and for external antennas an antenna gain up to 2 dBi for omni-directional antennas and up to 6 dBi for directional antennas. | Addition of a separate case for integrated antennas not accepted as this case is already covered by the two existing (generic) cases. |
| DECT Forum/6 | DECIDES | 1b | Technical | For external directive antennas 8 dBi is proposed (in line with CG simulations). This is to adjust to commercially available external antennas. | Change condition b: b. for integrated antennas an antenna gain of up to 4 dBi, and for external antennas an antenna gain up to 2 dBi for omni-directional antennas and up to 8 dBi for directional antennas. | Increase of antenna gain to 8 dBi not accepted as the compromise reached in previous discussions was for 250 mW plus 6 dBi However, the use of an 8 dBi antenna would be possible when the transmit power is reduced correspondingly (from 24 dBm to 22 dBm). |
| ETSI TC DECT/1 | Considering | i) | Technical / Editorial | ETSI has published the TR 103 089, which provides the relevant DECT radio parameters. It also gives a detailed description of the intended DECT system architectures and antenna properties/applications. It is proposed to add ETSI TR 103 089 as a background reference. | Add to paragraph i): and ETSI has provided an overview of considered DECT radio properties and intended applications in ETSI TR 103 089. | Accepted |
| ETSI TC DECT/2 | DECIDES | 1 | Technical | The Harmonized Standard EN 301 406 allows to increase the antenna gain by X dBi, if the transmit power is reduced by the same amount of X dB. This provision keeps the EIRP limit at the same level. It is proposed to include this possibility as a new condition. | Add a new condition c: c. if the power in condition a. is X dB below 24 dBm, then the dBi limits in condition b. are increased by X dB. | Principle accepted, but specifying the EIRP limit instead of the antenna gain |
| NEC/1 | DECIDES | 1b | Technical | 1) The success of our enterprise IP DECT systems depends to a large extent on our advanced method of over the air system synchronization. This means that, despite the latency of the IP system used to transport speech data to the access points, we can achieve accurate on-air timing. We regularly use antenna’s with 8dBi gain in order to aid with synchronization of large sites. This allows us to design a well-working system while minimizing the number of access points required. If the use of external antenna’s is further restricted, this will inevitably mean that we need to use more access points to cover the same area. 2) Simulations by PT1 Correspondence Group in May have shown no adverse effects when using 8dBi directional antennas for DECT. 3) In addition, directional antennas of less than 8dBi are not available from our antenna supplier. | To change the value of 6dBi for directional antennas to a value of 8dBi. | Increase of antenna gain to 8 dBi not accepted as the compromise reached in previous discussions was for 250 mW plus 6 dBi However, the use of an 8 dBi antenna would be possible when the transmit power is reduced correspondingly (from 24 dBm to 22 dBm). |