| Meeting Contribution |
| --- |
| Title: | Revision of ECC Decision(98)22 on Exemption from Individual Licensing of DECT equipment |
| Date: | 28.9.2012 |
| From (source): | Chairman of ETSI TC DECT |
| Contact(s): | guenter.kleindl@atos.net |
| To: | ECC-ETSI offficials meeting #16 |
| Contact(s): |  |

- Background

The ECC Decision(98)22 on “Exemption from Individual Licensing of DECT equipment, except fixed parts which provide for public access” was first published in October 1994. The last update was done in March 2007. (see included file below)

A new revision of the Decision was started by ECC WGRA and put on hold pending sharing studies carried out in SE7. These studies have been completed in the meantime. (see included file below)

The responsibility for the ECC Decision(98)22 was transferred by ECC to ECC PT1 after the closure of ECC WGRA. ECC PT1 now started the discussion on the revision of this Decision.

2. Issues

At the ECC PT1 meeting in Kristiansand, 17.-21.9.2012, a proposal was received

- to reduce the power level for DECT terminal equipment that CEPT administrations shall exempt from individual licensing and

- to move to “e.i.r.p.” notation for the transmitted power.

I am concerned about proposals to change the power level, that has been the same since it was agreed in 1992 and that is also included in EN 301 406 the Harmonized Standard for DECT.

I would like to note, that ETSI has never defined “e.i.r.p.” values for DECT.

TC DECT has not received any input to investigate this topic or any related issues.

3. Way forward

It is important to have a close cooperation between ECC and ETSI regarding these issues.