## Slide 1: FM50 drafting group 4
Mainz 6-9 March

## Slide 2: Criteria 1
Find agreement on simple questions (some already approved at FM50#3)
  RR article 5 region 1, changes needed?
  MA02revCO07 the allotment plan
  MA02revCO07 annex II (channelization, emission mask)
  MA02revCO07 cross border coordination procedures
  ECC DEC(03)02
Add explanatory text.

## Slide 3: RR article 5 region 1
Application | Compliance to the RR:
Application 1 (terrestrial broadcasting) | Yes (limited to audio broadcasting in footnote 345)
Mobile Broadband | Yes
MMD | Yes
Satellite Broadcasting | Yes, limited to audio broadcasting in footnote 345
[Satellite Mobile broaband] | No
[Satellite MM downlink] | No
PMSE | Yes
PPDR | Yes
BDA2GC | No

## Slide 4: MA02revCO07 (1)
Application | MA02revCO07 compatibility with the Plan (allotments)
Terrestrial broadcast | Yes
Mobile Broadband | No
MMD | No
Satellite Broadcasting | No
[Satellite Mobile braodband] | No
[Satellite MM downlink] | No
PMSE | Can use interleaved spectrum of the allotment plan as secondary service
PPDR | No
BDA2GC | No

## Slide 5: MA02revCO07 (2)
Application | MA02revCO07: compatibility with the enveloppe concept [channelisation given in Annex II (x contiguous channels of 1.7 MHz which may be aggregated to form 5.1 MHz channels, spectrum emission mask)]
Terrestrial broadcast | Yes
Mobile Broadband | could use aggregation of channels for downlink link but suboptimal. For the mobile transmitters appropriate procedure may need to be defined through mutual agreement.
MMD | could use aggregation of channels but suboptimal
Satellite Broadcasting | No (§ from SES)
[Satellite Multimedia] | No
PMSE | Yes, can fit several audio channels within a T-DAB channel (as a secondary service would not need to notify)
PPDR | could use aggregation of channels for downlink link but suboptimal. For the mobile transmitters appropriate procedure may need to be defined through mutual agreement.
BDA2GC | could use aggregation of channels for forward link but suboptimal. For the mobile transmitters appropriate procedure may need to be defined through mutual agreement.

## Slide 6: MA02revCO07 (3)
Application | Possibility to use the cross border coordination procedures in MA02revCO07
Terrestrial broadcasting | Yes [§ generic paragraph to add to section 6]
Mobile Broadband | need to develop procedure for mobile transmitters
MMD | The procedure could be used as the transmitters are fixed
Satellite Broadcasting | Not applicable, ITU coordination applies
Satellite Multimedia | 
PMSE | Not applicable, as a secondary service does not use the Maastricht procedure
PPDR | need to develop procedure for mobile transmitters
BDA2GC | Not applicable, CEPT wide service

## Slide 7: ECC DEC(03)02
Application | Compatibility with ECC DEC(03)02
Terrestrial broadcasting | No
Mobile Broadband | No
MMD | No
Satellite Broadcasting | Yes limited to audio broadcasting (may be complemented by a terrestrial component in areas where satellite signal is not available (considering f of ECC DEC(03)02)
Satellite Multimedia | 
PMSE | No
PPDR | No
BDA2GC | No