## Slide 1: Study on a) maximum transmit power for TVWS devices b) available amount of TVWS in Bavaria/Germany
Georg Schuberth
Radio Transmission Systems
Acknowledgement
The work leading to these results has received funding from the European Community's Seventh Framework Programme [FP7/2007-2013] under grant agreement n°248560.
Annex 1 to SE43(11)28

## Slide 2
COGEU results
estimating Pmax
To estimate Pmax and amount of available TVWS
methodology
parameters
assumptions
are required.

## Slide 3
estimating Pmax

## Slide 4
from ECC report 159, fmla. 4.3-4
Additional interference caused by a TVWS device can be included by an additional term:
assuming Gaussian signals (ECC report 159, fmla. 4.3-5:
allows to calculate IWSD:
estimating Pmax

## Slide 5
 | BS |  | UE |  |  |  | BS |  | UE | 
PR_co | 22 | dB | 22 | dB |  |  |  |  |  | 
PR_1 | -33 | dB | -13 | dB |  | Oth_1 | -13 | dBm | -20 | dBm
PR_2 | -40 | dB | -41 | dB |  | Oth_2 | -8 | dBm | -18 | dBm
PR_3 | -39 | dB | -42 | dB |  | Oth_3 | -19 | dBm | -26 | dBm
PR_4 | -48 | dB | -49 | dB |  | Oth_4 | -13 | dBm | -20 | dBm
PR_5 | -49 | dB | -50 | dB |  | Oth_5 | -8 | dBm | -18 | dBm
PR_6 | -50 | dB | -49 | dB |  | Oth_6 | -6 | dBm | -18 | dBm
PR_7 | -50 | dB | -52 | dB |  | Oth_7 | -5 | dBm | -16 | dBm
PR_8 | -51 | dB | -52 | dB |  | Oth_8 | -5 | dBm | -15 | dBm
PR_9 | -39 | dB | -39 | dB |  | Oth_9 | -6 | dBm | -14 | dBm
average parameters
Parameters taken from ECC report 148 (DVB-T interfered by LTE):
estimating Pmax

## Slide 6
 | Broadcast | 
TVWS | fixed (FR) | portable (PO)
Base station (BS) | dmin = 30 m Yagi antenna | dmin = 10 m Dipole antenna
User equipment (UE) | dmin = 20 m Yagi antenna | dmin = 2 m Dipole antenna
Downlink only (DO) | Higher BS antenna dmin = 50 m | Higher BS antenna dmin = 50 m
Assumptions:
Only receivers within coverage areas are protected
channels 40-60 are considered; ch>60 are assumed to be free
minimum distance between TVWS transmitter and DVB-T receiver
multiple interference not considered
simple propagation model
acceptable degradation of location probability due to TVWS device: 1%
estimating Pmax

## Slide 7
 | BS – DVB-T fixed | BS – DVB-T port. | UE – DVB-T fixed | UE – DVB-T port.
Oth | -19 dBm | -19 dBm | -25 dBm | -25 dBm
Min. dist. | 30 m | 10 m | 20 m | 2 m
Antenna gain | 9.15 dB | 2.15 dB | 9.15 dB | 2.15 dB
Coupl. gain | -49 dB | -46 dB | -45 dB | -32 dB
Pmax | 30 dBm | 27 dBm | 20 dBm | 7 dBm
Analytical result: Overloading limits TVWS device transmit power:
In most of the European nations it can be assumed that there is at least one broadcast coverage within n±9 of each channel at any location. Under this assumption the overload threshold in combination with the shortest possible distance between TVWS device and TV antenna determines an upper limit for the possible transmit power for TVWS device:
estimating Pmax

## Slide 8
estimating Pmax

## Slide 9
Location probability, ch. 36 … 44:
TVWS base station power map
ch 40, broadcast fixed reception:
estimating Pmax

## Slide 10
estimating Pmax

## Slide 11
Maximum TVWS Base Station transmit power at a location NE of Munich:
estimating Pmax

## Slide 12
Amount of TVWS in Bavaria
The concept of safety distance for estimating the amount of available TVWS in Bavaria
In document SE43(10)17 EBU proposed an interference margin. As an intermediate solution -10 dB were assumed 
IWSD = -98 dBm – 10 dB (noise limited)
PWSD = IWSD – coupling gain =
= -108 – path loss – 9.15 dB
Distance | Pmax
1 km | -18 dBm
2 km | -6 dBm
4 km | +5 dBm
5 km | 10 dBm
6 km | 13 dBm
10 km | 21 dBm
15 km | 28 dBm
20 km | 33 dBm

## Slide 13
safety distances:
cyan: 1 km
green: 5 km
yellow: 10 km
orange: 20 km

## Slide 14
safety
distance
1 km
safety
distance
5 km
safety
distance
10 km
safety
distance
20 km
only channel 45:
for channels
40 … 60:
TVWS mapped to area:

## Slide 15
TVWS mapped to area / mapped to population density

## Slide 16
FCC in the USA allows for white space devices a maximum transmit power of 40 mW (16 dBm), if operated in a channel adjacent to a used TV channel. If transmit power gets higher, up to 4 W EIRP (36 dBm), operation is only allowed in channels with at least one free channel separation to the next used TV channel.
Considering adjacent channels

## Slide 17
Our investigations were performed with moderate values for protection ratios, overload threshold, etc. Even with these moderate parameters results show that
in portable broadcast areas TVWS device Pmax is limited to below ~20 dBm (i.e. operational range of approx. 1 km).
outside portable broadcast areas Pmax may be somewhat higher, however is finally limited by overloading threshold
So, viable scenarios for TVWS use could be:
In areas with portable broadcast coverage: low power transmit systems, like WiFi
In rural areas / isolated residential areas a downlink only concept (with some limitations) could provide a reasonable means to provide broadband internet supply to area.
Summary
Notes: WiFi in urban areas:
  Better penetration characteristics allow improved in house LAN operation
  ISM bands are overstrained esp. in dense urban areas, where TVWS usage could bring a significant release
  If –for low transmit power- operation at channels adjacent to TV used channels is possible, there is a reasonable amount of TVWS available
broadband internet provision in rural areas
If larger minimum distances can be assumed the downlink only (DO) concept could provide a reasonable means to provide broadband internet supply to area.
  Usually the download traffic is much higher than upload traffic, so using TVWS for downlink and mobile communication bands for uplink seems reasonable.
  Usually in rural areas wired broadband access is not available due to high infrastructure costs, so this TVWS usage is especially appropriate for rural areas.

## Slide 19: Vielen Dank für Ihre Aufmerksamkeit.
Institut für Rundfunktechnik
Floriansmühlstraße 60
80939 München
Tel. +49-(0)89-32399-0
Fax +49-(0)89-32399-351
E-Mail: name@irt.de
Die Folien/Dokumente sind durch das Urheberrecht geschützt. Eine Vervielfältigung ist nur mit Genehmigung des Verfassers gestattet. Dieser Urheberrechtshinweis darf nicht entfernt werden.
[Name]
[Sachgebiet]