## Slide 1: Introduction to SEAMCAT
EUROPEAN COMMUNICATIONS OFFICE | Nyropsgade 37, 4th floor 1602 Copenhagen Denmark | Telephone: + 45 33 89 63 07 Telefax: + 45 33 89 63 30 | E-mail: jean-philippe.kermoal@eco.cept.org Web Site: http://www.cept.org/eco
Jean-Philippe Kermoal - SEAMCAT Manager (ECO) June 2014

## Slide 2: Outline
Spectrum Engineering
SEAMCAT
Conclusions

## Slide 3: Spectrum engineering challenges
The requirement for global compatibility amongst many radio systems within a congested radio spectrum
introduction of new radio applications
technological
regulatory
economic considerations
increasing penetration of the existing radio applications

## Slide 4: Need for spectrum sharing
There is no more “empty” spectrum
Proposed new systems have to find way of “sharing” with some of existing systems
Thus the need for spectrum engineering and optimisation:
  to find which existing radio systems are easiest to share with, and then
  determine the “sharing rules”
Sharing methods: space/frequency/time
Sharing implementation: Agile (cognitive) or Rigid-design (traditional)

## Slide 5: Defining the sharing rules
Analytical analysis, usually by worst-case approach:
Minimum Coupling Loss (MCL) method, to establish rigid rules for minimum “separation”
Statistical analysis of random trials
The Monte-Carlo method, to establish probability of interference for a given realistic deployment scenario
That is where SEAMCAT comes into picture!

## Slide 6: Strategic tool for CEPT
For performing compatibility/sharing studies
Used in generating studies for ECC/CEPT Reports
As a Reference tool
Recognised at ITU (Rep. ITU-R SM.2028-1)
As an agreed work platform
Project Teams (PTs) can focus on the input parameters and not on the algorithm
Sharing simulation between proponents ease the trust in the results
For educating future generation of spectrum engineer (Administrations, Industry or University)

## Slide 7: Usage in and outside CEPT
Source: google analytics on the www.seamcat.org download page in 2013.
2013 survey on the number of SEAMCAT download: about 1200 download

## Slide 8: History
Developed in CEPT as a co-operation between National Regulatory Administrations, ECO and industry
First released in Jan-2000, then gradually developed in several phases
Latest version 4.1.0 (October 2013)
Freely downloadable from ECO website (www.seamcat.org)

## Slide 9: Purpose
SEAMCAT is designed for:
  Co-existence studies between different radio systems operating in same or adjacent frequency bands
  Any type of radio systems in terrestrial scenarios
  Extended to cellular system like CDMA and OFDMA
  Quantification of probability of interference between various radio systems
Not designed for system planning purposes
Based on Monte-Carlo generation

## Slide 10: Typical examples of modelled system
Mobile:
  Land Mobile Systems
  Short Range Devices
  Earth based components of satellite systems
Broadcasting:
  terrestrial systems
  DTH receivers of satellite systems
Fixed:
  Point-to-Point and Point-to-Multipoint
  ... and more

## Slide 11: Installing SEAMCAT
On-line Webstart:
Internet connection is needed at least for the installation; during later runs Internet used (if available) to check for updated version
Off-line
(Windows, Linux, Mac)
(Windows only)
1GB RAM needed
Java Runtime Environment (RTE) (version 1.7 and above)
FREE DOWNLOAD

## Slide 12: Open source code
Open source in Java
Source code available upon request
2 steps procedure:
  License agreement to sign
  Register to the “seamcat source code” group

## Slide 13: Main Interface
Windows-oriented
Main element – workspace.sws
Simulations input data – scenario:
Equipment parameters, placement, propagations settings, etc.
Simulation controls:
number of events etc..
Simulation results:
dRSS/iRSS vectors, Pinterference, Cellular structure

## Slide 14: Graphic interface (1/1)
Easy view of parameters at a glance
Easy comparison of workpsaces
Graphical reminders (tooltip)

## Slide 15: Graphic interface (1/2)
Shows positions and budget link information of the victim and interfering systems
Overview of results (dRSS, iRSS)
Intuitive check of simulation scenario

## Slide 16: Libraries and Batch
Easy to create workspaces with predefined libraries
  Edit, import, export
Easy to run sequentially workspaces
  Batch operation
  Intuitive use

## Slide 17: Welcome + News History
Welcome + News
History
Welcome + News

## Slide 18: Multiple vectors display
Calculated vectors or external vectors
Statistics and signal type

## Slide 19: Comparing propagation model
Compare two or more propagation models
Results in linear or log format

## Slide 20: Conclusions
Sharing rules are important element of spectrum optimisation process
Unless some intelligent interference avoidance is implemented in radio systems, the careful choice of sharing conditions is the only means for achieving successful co-existence and optimal spectrum use
Statistical tool SEAMCAT is a powerful tool for such analysis
Strategic tool for the CEPT
Reference tool – recognised at ITU
World wide usage
Free tool to run on any operating system platform

## Slide 21: Thank you - Any questions?