## Slide 1: 6 GHz WAS/RLAN potential in CEPT
Stephen Talbot (Chair of FM57 “6 GHz RLAN”, CEPT Work on WAS/RLAN in 5925 – 6425 MHz)
Dynamic Spectrum Alliance Global Summit – June 2019

## Slide 2: ECC
March 2017 – Work item agreed in ECC for 5925 – 6425 MHz
Convention is that technical and regulatory discussions are split
Work on the “technical feasibility” for WAS/RLAN in the band
Initial tasks directed towards technical study (“this isn’t 5 GHz”)
ECC Report 302 – technical study published end May 2019

## Slide 3: ECC and European Commission
EU Mandate delivered to CEPT in December 2017
Two stage process, CEPT Reports A and B
Reporting technical feasibility : CEPT Report A (July 2019)
Defining harmonised technical conditions : CEPT Report B (July 2020)
CEPT recently agreed work item :ECC Decision for WAS/RLAN in 6 GHz

## Slide 4: Key Findings of CEPT Report A on 5925-6425 MHz 1/2
Adopted for ECC public consultation at WGFM#94 on 7 June 2019
Key findings of Report A:
Compatibility and coexistence between RLAN and existing services within and adjacent to the band 5925-6425 MHz is technically feasible under certain conditions. For example, indoor only deployment with a maximum EIRP in the range of 200-250 mW.
Coexistence with CBTC systems and Road ITS up to 5935 MHz (and in certain countries up to 5975 MHz) would be technically feasible assuming suitable measures such as a guard-band and requirements on RLAN in band and/or out-of-band emissions.
Higher power devices and outdoor devices present a risk of harmful interference to FS, FSS, Communication based train control (CBTC) systems and Road Intelligent Transport System (ITS) incumbents without mitigations.

## Slide 5: Key Findings of CEPT Report A on 5925-6425 MHz 2/2
Key findings of Report A:
Feasibility of outdoor deployment and high-power access points (APs) would require additional studies to address the interference to the incumbent users. Additional work to address these scenarios would occur under a separate ECC deliverable.
CEPT Report B, which will be developed in response to Task 2 of the EC Mandate, will provide a regulatory framework including all relevant technical conditions.
Complementary studies and analyses are still required on the FS short-term protection criterion for WAS/RLAN indoor only deployment as well as on potential RLAN portable devices that operate outdoor with power levels significantly lower than that for indoor use.
In addition, investigations may include innovative sharing solutions for geographical protection of incumbent applications.

## Slide 6
ECC Contact | Web www.cept.org/ecc
ECO Nyropsgade 37, 4th floor DK-1602 Copenhagen Tel:+45 33 89 63 00 E eco@eco.cept.org | 

## Slide 7
Preparing for UK implementation for 6 GHz RLAN
Stephen Talbot, Head of International Spectrum Policy, Consumer and External Relations Group, Ofcom

## Slide 8
UK Process
Original ideas for RLAN 6 GHz came from outside the UK
UK has actively participated in the work in CEPT
Still assessing impact on existing services, looking to undertake practical testing
Next step to potential national rulemaking would be a Public Consultation
Supported the recent WI for ECC Decision in 5925 – 6425 MHz

## Slide 9
Thank you. . . .