## Slide 1: 10th International Electronic Communications Regulators Conference 8th May 2015 Future of mobile: 4G and Beyond
Eric Fournier
Chairman, Electronic Communications Committee

## Slide 2: Spectrum management in Europe: 3 institutions
Council of the EU
European Parliament

## Slide 3: Harmonisation process within CEPT and EU
Spectrum Policy Strategy
ECC
RSCOM
Commission
RSPG opinions
ECC Decision
EC Decisions
Industry
Spectrum Decision
EC mandates
CEPT Reports
RSPP Radio Spectrum Policy
Program EU DEC 243/2012/UE
CPG
WRC-15 preparation

## Slide 4: ECC harmonises spectrum for mobile broadband
  Nine frequency bands harmonised for mobile broadband (4G) through ECC Decisions
  ECC decisions for mobile broadband are technology neutral (ie, not only “4G”)
    Use of the “Block Edge Mask” concept to define technology neutral conditions
    For 900 and 1800 MHz band, the ECC decisions have listed technology which can be implemented (GSM, UMTS, WiMax, LTE)
  European harmonisation is not sufficient
    Role of “IMT identification” in the ITU Radio Regulations (RR)
    ECC prepares WRC-15: opportunity for more spectrum, more harmonisation for 4G

## Slide 5: Frequency bands already harmonised for mobile broadband
Band | Size (MHz) | Ref
800 MHz | 2x30 | ECC DEC(09)03
900 MHz | 2x35 | ERC DEC(94)01 & ERC DEC(97)02 &ECC DEC(06)13
1452-1492 MHz | 40 | ECC DEC(13)03
1.8 GHz | 2x75 | ERC DEC(95)03 & ECC DEC(06)13
2 GHz | 2x60 | ECC DEC(06)01
2.6 GHz | 2x70+50 | ECC DEC(05)05
3.4-3.8 GHz | 400 | ECC DEC(11)06
 | Sub-Total : 1030 MHz | 
700 MHz | 2x30 + 20 | ECC DEC(15)01 (?)
2.3-2.4 GHz | 100 | ECC DEC(14)02
 | Total : 1210 MHz | 

## Slide 6: The example of the 700 MHz band
  ECC Decision adopted in March 2015
    2x30 MHz in line with the “APT” band plan : equipment available
    Option for 20 MHz SDL in the centre gap
    Other options : PPDR, M2M, PMSE
  Target date in the RSPG opinion : 2020, with 2 years “flexibility”
    Cross-border agreement for broadcasting below 694 MHz, before 2017
    470-694 MHz : priority on broadcasting until at least 2030 but Member states have some flexibility for mobile downlink
  WRC-15 AI 1.2 : European position in line with ATU and ASMG

## Slide 7: 2300-2400 MHz
  ECC Dec(14)02
    100 MHz of potential unpaired spectrum (LTE TDD)
    Example of services to be protected : aeronautical telemetry, cordless camera (+ WiFi >2400 MHz)
  First implementation of “Licensed Shared Access” within Europe
    Static or dynamic (=geolocation/database) depending on the incumbent application
    Guidance given on the protection of cordless camera in a future ECC Recommendation

## Slide 8: LSA Approach ?
  “A regulatory approach aiming to facilitate the introduction of radiocommunication systems operated by a limited number of licensees under an individual licensing regime in a frequency band already assigned or expected to be assigned to one or more incumbent users. Under the Licensed Shared Access (LSA) approach, the additional users are authorized to use the spectrum (or part of the spectrum) in accordance with sharing rules included in their rights of use of spectrum, thereby allowing all the authorised users, including incumbents, to provide a certain Quality of Service (QoS)”.

## Slide 9: 3400-3800 MHz
ECC revised in 2014 the ECC Decision(11)06
    fostering the harmonisation
    opportunity for LTE TDD development
    new round of authorizations soon in Europe to respond to EU obligations
C band is lightly used by earth stations in Europe and sharing is feasible with individual earth stations
WRC-15 :
    draft ECP for 400 MHz of mobile allocation and IMT identification
    Satellite is important for infrastructure in particular in equatorial countries and draft ECP for no change in 3800-4200 MHz

## Slide 10: L band : 1427-1518 MHz
1452-1492 MHz already harmonised by ECC for Supplemental Downlink
Draft ECP for identifying the band 1427-1518 MHz for IMT,
91 MHz of additional, contiguous, spectrum …probably the last opportunity for new spectrum for 4G in lower bands
ECC will define harmonised technical conditions for the whole band after WRC-15

## Slide 11: From 1G to 5G
1980
1990
2000
2010
2020
Max.
Bit rate
1G Analogue (voice)
GSM
GPRS
EDGE
UMTS
HSDPA
LTE
LTE-Advanced
5G ?
9 Kbit/s
54 Kbit/s
384 Kbit/s
5 Mbit/s
42 Mbit/s
150 Mbit/s
1 Gbit/s
10 Gbit/s ?
900 MHz
2100 MHz
900 MHz
1800 MHz
800 MHz
1800 MHz
2.6 GHz
Years
2G
3G
4G

## Slide 12: What about 5G ?
5G could be used in 4G spectrum under technology neutral policy
… but some 5G features may significantly impact spectrum policy
    Use of wider bandwidth and higher spectrum
    Better adjacent band performance, sharing mechanism
    Small cells
    Blurring the distinction between access and backhauling
Activities to support an agenda item for bands > 6 GHz at WRC-19 … and 5G is part of the new ECC strategic plan !

## Slide 13
Thanks ...