## Slide 1: WiFi Alliance 18th October 2016 Spectrum for WiFi – ECC Actions
Eric Fournier
Chairman, Electronic Communications Committee

## Slide 2
RADIO SPECTRUM POLICY GROUP (RSPG)
European regulatory environment

## Slide 3
Structure of the ECC
Structure of the ECC
Electronic
Communications Committee
Chairman: E. Fournier (F)
Vice-Chairmen: S. Pastukh (RUS) J. Afonso (POR)
European
Communications Office
Director: P. Christensen (DNK)
Deputy Director: B. Espinosa (F)
Steering Group
WG FM
Frequency
Management
Chairman:
T. Weilacher (D)
Vice-Chairmen:
C. Reis (POR)
S. Talbot (G)
WG SE
Spectrum
Engineering
Chairman:
K. Loew (D)
Vice-Chairmen:
J. Duque (POR) k. Bejuk (HRV)
WG CPG
Conference
Preparatory Group
Chairman:
A. Kühn (D)
Vice-Chairman:
G. Osinga (HOL) A. Vallet (F)
WG NaN
Numbering
and Networks
Chairman:
J. Vallesverd
(NOR)
Vice-Chairman:
E. Greenberg (G)
F. Dragomir (ROU)
IMT-Matters
Chairman:
S. Green (G)
Vice-Chairmen:
P. Toivonen (FIN)
ECC PT1
Updated: October 2016

## Slide 4: ECC and WiFi
  2.3-2.4 GHz harmonisation for MFCN –
    Protection of WiFi @ 2.45 GHz
  5 GHz WiFi – Existing bands and possible extension
    EC mandate for possible extension – CEPT Report 64
    WRC-19 preparation
  SRD/IoT in the bands 800/900 MHz
    IEEE 802.11ah
    Addendum to CEPT Report 59
  TV White Space
  WiGig in the band 57-66 GHz
  WiFi in cars, trains, aircraft

## Slide 5: 2.3-2.4 GHz - ECC harmonisation
  2.3-2.4 GHz harmonised for broadband wireless systems:
    “LTE” blocks multiple of 5 MHz
    68 dBm/5 MHz per antenna
  Protection of 2.45 GHz WiFi
    “Restricted blocks” 2390-2400 MHz
    eirp shall not exceed 45 dBm/5 MHz
  Outstanding issue
    Measurements: need to improve WiFi receiver characteristics
    Liaison with ETSI TG11

## Slide 6
Area / MHZ | 5150-5250 | 5250-5350 | 5350-5470 | 5470-5725 | 5725-5850 | 5850-5925
Europe | Yes | Yes | No | Yes | No | No
US | Yes | Yes | No | Yes | Yes | No
 | 200 mW Indoor | 200 mW DFS Indoor |  | 1 W DFS outdoor |  | 
Globalstar
Radars
Copernicus
DSRC tolling
SRD
ITS
FSS
Telemetry
Space Altimeters
Situation in the 5 GHz RLAN bands
Amateur
BFWA
DA2GC

## Slide 7: WRC-19 AI1.16 – Preparatory ECC studies
Today: No satisfying conditions to protect incumbent services in 5350-5470 & 5725-5925 MHz (see draft CEPT Report 64)
WRC-19 Agenda Item 1.16
    Accommodating WLAN in 5350-5470 MHz, 5725-5850 MHz,5850-5925 MHz ?
    Removing indoor restriction in 5150-5350 MHz ?
    Mitigation techniques (EESS, radars …) ?
  CPG/PTD will prepare AI1.16 and ITU WP5A studies
  CPG takes also account of other interests within WRC-19 AI IoT, M2M (9.1.8), ITS (1.12)

## Slide 8: 802.11 ah in the 800/900 MHz band
  Addendum to CEPT Report 59 in public consultation in November “possibilities for a harmonisation approach for the bands 870-876 MHz, 915-921 MHz & 862-868 MHz”
  IEEE 802.11ah and smart home as “generic SRD” 25 mW
  Under discussion, new “mandatory” harmonisation:
    863-868 MHz
    Few MHz within 915-921 MHz

## Slide 9: TV White Space
  Toolbox available for white space:
    ECC Report 159 “Technical and operational requirements for the possible operation of cognitive radio systems in the “white spaces” of the frequency band 470-790 MHz”
    ECC Report 185: “Definition of technical and operational requirements for WSD in 470-790 MHz”
    ETSI harmonised standard EN 301 598
  … but no harmonisation, left to national decision
  significant evolution in the past years in the UHF band
  no strong market signal from US/UK

## Slide 10: WiGig in the band 57-66 GHz
  Existing regulation:
    40 dBm eirp (13 dBm/MHz)
    No fixed outdoor installation
  Other applications in this spectrum
    Fixed Service in 57-59 GHz, 59–62 GHz AND 64–66 GHz
    ITS in 63-64 GHz
  Possible relaxation of technical conditions?
    Ongoing ECC discussions on possibility to relax restrictions (eirp / fixed outdoor)
    General objective of improving spectrum efficiency in the band

## Slide 11
Thanks ...