## Slide 1: Spectrum solutions for IoT connectivity
The 7th Annual Internet of Things European Summit
18-19 May, Brussels
Eric Fournier
ECC Chairman
eric.fournier@anfr.fr

## Slide 2: An horizontal solution: from 2G to 4G
LTE-based M2M (LTE-eMTC)
    1.4 MHz and 3 MHz bandwidth
Narrowband M2M
EC-GSM-IoT and NB-IoT
    200/180 kHz bandwidth
  A new Work Item in ECC PT1
  “To study the suitability of the current technical conditions
  of harmonised MFCN bands for LTE-based M2M and NB M2M”
ECC Report 242 on IoT spectrum in the 733-736 MHz / 788-791 MHz band :
reluctance for dedicated spectrum + other usage of the band
no further action

## Slide 3: An « ultimate » horizontal solution ? 5G
5G targets IoT market
5G features : network slicing, low energy consumption, scalability…
Lower frequency range for coverage, reliability, low latency ?
ITU-R M.2083-0
  Ensuring that 5G can be introduced in existing bands
  Including 3400-3800 MHz !
  Issue of other bands with FDD channelling arrangements
  WRC-19 agenda item 1.13 on 5G spectrum above 24 GHz
  All bands proposed by Europe are in the list of bands to study
  Many bands potentially for Europe : 31.8-33.4 GHz, 24.25-27.5 GHz, 40.5-43.5 GHz, 66-71 GHz …

## Slide 4: Unlicensed bands for IoT
  “user operated” : PAN, RFID, home automation …
  “network operated” : Low Power Wide Area (Sigfox, LoRa, telemetry), Mesh networks, aeronautical/satellite ?
The new Eldorado : the 800/900 MHz band
ECC will define more flexible conditions in 862-870 MHz
ECC has defined « à la carte » harmonisation in 870-876 MHz and 915-921 MHz (existing users : Governmental, E-GSM-R)
915-921 MHz has potential for worldwide harmonisation
Partial but “mandatory” implementation for EU under discussion for beginning 2017 ?
  Other bands : 169 MHz, 433 MHz, 2.45 GHz ..
  A new band contemplated: 1900-1920 MHz

## Slide 5: Spectrum solutions for vertical IoT ?
TTT
5795
ITS NonSaf.
ITS Safety
ITS Ext.
5925
5855
5875
5905
Transport
5815
Urban rails (CBTC)
WAS/RLANs
ITS-G5 vs LTE-V2X
Industry
Automation
  Existing use in 2.45 GH and in 5725-5875 MHz (400 mW+DFS and DAA+ registration/notification)
  “Wireless Industrial Automation requires an additional dedicated spectrum of 80 MHz in the range of 1,4 GHz to 6 GHz that is worldwide available”
  1900-1920 MHz ?
Health
  Medical Body Area Network in 2483.5-2500 MHz,
  AMI in various bands

## Slide 6: PMR solutions for IoT
  Private Mobile Radio (80 MHz, 150 MHz, 400 MHz) has always provided solutions for metering for utilities (transport, energy …)
  Other bands needed for PMR/IoT ?
  VHF bands (47-88 MHz)
  Bands higher than 1 GHz ?
  Case of Railways :
  future of GSM-R ?
  Moving to LTE/IoT ?
  ECC work on 410-430 and 450-470 MHz for LTE/IoT
  Shared IoT networks? National IoT platforms?
  Remaining needs for specific narrowband PMR/IoT
  Other usages : PMR, PPDR, radiolocation, governmental …

## Slide 7: For more information http://www.cept.org/ecc/