## Slide 1: Principle of Monte-Carlo in a SEAMCAT environment
European Communications Office
Jean-Philippe Kermoal - SEAMCAT Manager (ECO)
June 2012
(Jean-Philippe.Kermoal@eco.cept.org)
EUROPEAN COMMUNICATIONS OFFICE | Nansensgade 19 DK-1366 Copenhagen Denmark | Telephone: + 45 33 89 63 00 Telefax: + 45 33 89 63 30 | E-mail: eco@eco.cept.org Web Site: http://www.cept.org/eco

## Slide 2: Outline
Sharing/Compatibility studies
Conclusion
Event generation
MCL vs Monte-carlo approach

## Slide 3
Sharing: between different radio systems operating in the same frequency bands (ERC Report 68)
Compatibility: between different radio systems operating in the adjacent frequency bands
Analytical analysis: MCL (worse case)
Statistical analysis: Monte-Carlo method
Sharing/compatibility
studies

## Slide 4
The stationary worst-case is assumed
Wanted
Signal
Victim
Interferer
Dmin, or minimum frequency separation for D=0
  However such worst-case assumption will not be permanent during normal operation and therefore sharing rules might be unnecessarily stringent – spectrum use not optimal!
The MCL approach

## Slide 5
Repeated random generation of interferers and their parameters (activity, power, etc…)
  After many trials, not only unfavourable, but also favourable cases will be accounted, the resulting rules will be more “fair” – spectrum use optimal!
Wanted
Signal
Inactive
Interferer
Victim
Active
Interferer
t=t0
t=t1
t=ti
Monte-Carlo approach

## Slide 6
User will need to define the distributions of various input parameters, e.g.:
  How the power of interferer varies (PControl?)
  How the interferer’s frequency channel varies
  How the distance between interferer and victim varies, and many others
Number of trials has to be sufficiently high (many 1000s) for statistical reliability:
  Not a problem with modern computers
Monte-Carlo Assumption

## Slide 7
Positioning of two systems in frequency
Powers
Masks
Activity
Antenna
Etc...
Scenario parameters
Distribution
Pattern
Double / integer field
Function

## Slide 8
Random generation of transceivers
Link budget
Signal values
Only 1 victim link
MANY interfering links
Event generation

## Slide 9
Succession of snapshots…
VR
WT
1) Calculate d, Ptx, GaTx, GaRx, L
2) Calculate dRSSi
dRSS
Snapshot#
iRSS
Snapshot#
IT
WR
1) Calculate d, Ptx, GaTx, GaRx, L
2) Calculate received signal, if PC, adjust Ptx
1) Calculate d, Ptx, GaTx, GaRx, L
2) Calculate iRSSi
VR
WT
IT
WR
How event generation works*
(*) Except CDMA/OFDMA systems

## Slide 10
Vectors for useful and interfering signals:
Results of event generation
dRSS
iRSS

## Slide 11: Evaluating probability of interference
        - For each random event where dRSS>sensitivity:
Noise Floor (dBm)
Desired signal value (dBm)
Interfering signal (dBm)
C/Itrial > C/Itarget?
Interference (dB)
- If C/Itriali >C/Itarget: “good” event
- If C/Itriali <C/Itarget: “interfered”
- Finally, after cycle of Nall events:
Overall Pinterference= 1- (Ngood/Nall)dRSS>sens
dRSS -> (C)
iRSS -> (I)

## Slide 12: CDMA results
Initial capacity: Number of connected UEs before any external interference is considered.
Interfered capacity: Results after external interference is applied.
Excess outage, users: How many UEs were dropped due to external interference.
Outage percentage: Percentage of UEs dropped due to external interference.

## Slide 13: OFDMA results
Capacity results +
Non interfered bitrate: bitrate before any external interference
interfered bitrate: bitrate after external interference is applied.

## Slide 14: Conclusions
Versatile tool to configure victim and interferer
SEAMCAT returns the following results
Victim system | Intereference criteria
Classical (i.e. non CDMA/OFDMA module) | Probability of interference based on C/I, C/(I+N), (N+I)/N, I/N
CDMA | Capacity loss (i.e. number of voice users being dropped)
OFDMA | Bitrate loss (i.e. number of bit rate lossed compared to a non interfered victim network) Capacity loss (i.e. number of voice users being dropped)

## Slide 15: Thank you - Any questions?