## Slide 1: Overview of Systems in SEAMCAT
European Communications Office
Jean-Philippe Kermoal - SEAMCAT Manager (ECO)
June 2012
(Jean-Philippe.Kermoal@eco.cept.org)
EUROPEAN COMMUNICATIONS OFFICE | Nansensgade 19 DK-1366 Copenhagen Denmark | Telephone: + 45 33 89 63 00 Telefax: + 45 33 89 63 30 | E-mail: eco@eco.cpet.org Web Site: http://www.cept.org/eco

## Slide 2: Outline
CDMA system
OFDMA system
System type
Conclusion
Simple interface
Exercise #5
”Generic” system

## Slide 3: System type
Generic
CDMA
OFDMA

## Slide 4: Generic system
Start
While i=1,N
Generate position data of VLT, VLR
Calculate dRSSi
dRSS vector
While i=1,N
Generate position data of ILTj, ILRj
Calculate iRSSi,j
iRSS vector
While j=1,M
Calculate iRSSiSUM
dRSS, iRSS to ICE
A
B
C
D

## Slide 5: Simple and harmonised interface
Add
Duplicate
Delete
Multiple interferer generation
On-line Help
Workspaces
Interfering links

## Slide 6: CDMA/OFDMA modelling
Modelling of cellular systems as victim, interferer, or both:
  Quasi-static time within a snapshot
  One direction at a time (uplink or downlink)
CDMA
  Voice traffic only
  Particular CDMA standard defined by setting Link Level Data (CDMA2000-1X, W-CDMA/UMTS)
OFDMA
  LTE

## Slide 7: CDMA system modelling
First a succession of snapshots are run without interference, gradually loading the system to find the target non-interfered capacity per cell
apply interference and note the impact in terms of how many of initial users were disconnected
Generate position data of Wtj, Vrj
While j=1, L
Iterative process of power balancing in CDMA cells
Record dRSSi or other parameter, e.g. non-interfered CDMA capacity
Start
While i=1, N
Generate position data of Itk, Wrk
Calculate iRSSi,k
While k=1, M
Repeat iterative process of power balancing in victim CDMA cells, now with iRSS present as external impact
(N) records of interference impact
Record impacti of interference, e.g. loss of CDMA capacity
To further engines
CDMA as victim
Generate position data of Itj, Wrj
C
D
While j=1, M
Iterative process of power balancing in CDMA cells
Calculate iRSSi,j
While j=1, M
CDMA as
interferer

## Slide 8: CDMA vs OFDMA simulation
CDMA
CDMA performs a power tuning process when surrounded by two tiers of auxiliary cells, and total cluster of 19.
OFDMA
OFDMA performs an iterative process of assigning a variable number of traffic sub-carriers and calculating the overall carried traffic per base station.
OFDMA systems similar to CDMA systems
Except: After the overall two-tiers cellular system structure (incl. wrap-around) is built and populated with mobiles

## Slide 9: CDMA UL and DL as victim
CDMA UL
Noise rise is measured as the linear average of dB values – across all 19/57 base-stations
CDMA DL
Number of users that can fit into the system in 80% of the trials.
Red: <80% has been reached (i.e. too many users in the system – or not all trials yet complete)
Green: =80%
Yellow: >80% of the trials are successful (too few users in the system).
SEAMCAT stops when this dial stops in the green area after all trials completed.

## Slide 10
Modelled cellular system
Modelled cellular system (i.e. CDMA or OFDMA)
Two auto-generated tiers of auxiliary CDMA cells
Other radio system, counter-part in interference simulation
Interferer-Victim distance

## Slide 11
Several options
Application of Wrap-Around technique for calculation of distance to closest BS produces effect of “endless” uniform network
Only available in 2-tiers option

## Slide 12
legend
Cellular system last event
legend
BS antenna
BS or MS info display
General system info:
Cell specific info
Connected - voice active user
Active link
Inactive link
Dropped user
CDMA interferer
Detailed insight into simulated data for modelled CDMA/OFDAM system

## Slide 13: Network-edge case
Instead of centre cell, takes the cell at the edge cluster as a reference cell
Wrap-around formulas adjusted as if no other cells are located beyond that cell
cross-border or similar interference scenarios

## Slide 14: CDMA/OFDMA GUI (1/2)
2 tabs: General settings and Positioning

## Slide 15: CDMA/OFDMA GUI (2/2)

## Slide 16: Exercise #5
Victim: OFDMA DL
  5 active users (with 50 subcarrier per BS)
  Capacity (Initial users per BS):10
Interferer: DVB-T BS
  Power = 55 dBm
  SEM: DVB-T
Simulation control: 30 events (fast)

## Slide 17: Conclusions
Harmonised interface between generic and CDMA/OFDMA modules
Versatile tool to configure victim and interferer

## Slide 18: Thank you - Any questions?