|  | Working Group Frequency Management Project Team FM PT51 PMSE Issues | Doc. FM51(12)048Rev1 |
| --- | --- | --- |
| ECO, Copenhagen, 28 – 30 November 2012 |  |
| Date issued: 27 November 2012 Source: ECO Subject: Summary and preliminary analysis of the responses to the WG FM questionnaire on PMSE (Version 4) |

Summary: This document provides a summary and a preliminary analysis of the responses received to the questionnaire on PMSE developed by FM51 and agreed by WG FM at its 74th meeting.

Proposal: To be considered by FM51. Some elements may be used by FM51 in its current activities (revision of ECC Report 002, CEPT Reports in response to EC Mandate, revision of ERC/REC 25-10...).

Background: The document contains a summary of the responses and a preliminary analysis for each of the bands dealt with in the questionnaire. The set of full responses sent by the administrations is annexed to this document. It is intended to update this document on a regular basis through exchange between the ECO and the national administrations contact points. Version 1: 9 July 2012 A total of 29 CEPT countries provided a response to the questionnaire. Amongst those, one administration mentioned that it was not in position to provide relevant information because of an ongoing review process of its national frequency table allocation and one administration provided information limited to 5 of the 19 frequency bands under consideration. Although some of the other responses may not be fully complete for all specific items, it is considered than this set of responses provide a quite representative snapshot of the PMSE use across CEPT. Administrations are invited that the information provided in this summary is consistent with their situation and to send to the ECO any correction or update if relevant.

Version 2: 12 July 2012 With the addition of 2 new responses (MLT, E), this revision includes now the responses from 31 CEPT countries. Furthermore, a few modifications or clarifications have been made to the responses by the concerned administration (FIN, LTU, F) and reported as appropriate into the summary included in this document. Version 3: 18 September 2012 This 3rd version includes the responses from 32 CEPT countries (addition of POR). Furthermore, one correction has been made to the responses by one administration (HUN). The summary has been updated as appropriate. Version 4: 27 November 2012 As a result of the introduction of version 3 to the September 2012 meeting of WG FM, two additional responses were sent to the ECO from . Thus, the 4th version includes the responses from 34 CEPT countries and a further update of the summary as appropriate List of responses (27 November 2012) Annex Country Code Country Name Annex Country Code Country Name 1 MNE Montenegro 18 F France 2 CYP Cyprus 19 HRV Croatia 3 LUX Luxembourg 20 SVK Slovakia 4 MKD The Former Yugoslav Republic of Macedonia 21 SRB Serbia 5 ISL Iceland 22 I Italy 6 FIN Finland 23 S Sweden 7 DNK Denmark 24 HNG Hungary 8 CZE Czech Republic 25 AUT Austria 9 SUI Switzerland 26 BUL Bulgaria 10 GEO Georgia 27 G United Kingdom 11 HOL Netherlands 28 RUS Russian Federation 12 NOR Norway 29 IRL Ireland 13 EST Estonia 30 MLT Malta 14 BLR Belarus 31 E Spain 15 TUR Turkey 32 POR Portugal 16 LTU Lithuania 33 GRC Greece 17 D Germany 34 LVA Latvia

1 Band 29.7-47.0 MHz (Rec. 70-03)

Summary table

| Annex - Country | Band available? | Licensing regime | Technical conditions | PMSE type | Other use | Change expected? |
| --- | --- | --- | --- | --- | --- | --- |
| 1- MNE | Yes | License exempt Website Details in Annex 1 | Rec 70-03 Annex 10 | Radiomics | Defence systems; SRD - Wireless applications in Healthcare (30-37.5 MHz); SRD- Inductive applications (148,5 kHz – 30 MHz); SRD- Model Control (34,995–35,225 MHz; 40,665/40,675/ 40,685/40,695 MHz ); Radio astronomy(37,5 – 38,25 MHz); Meteor scatter communications(39.0-39.2 MHz); ISM; Wind profiler radars(46–68 MHz); PMR(T/R 25–08) | No |
| 2-CYP | Yes | License exempt for 29.7 - 34.9 MHz and 37.5 – 47.0 MHz Reviewed on a case-by-case basis for 34.9-37.5 MHz Details in Annex 2 | Rec 70-03 Ver 30/05/07 | Radiomics |  |  |
| 3- LUX | Yes except 34.995 - 35.225 MHz , reserved for flying models | License exempt Details in Annex 3 | Rec 70-03 A10a | Radiomics | non-specific SRDs, ISM, medical implants or flying models | No |
| 4- MKD | Yes | License exempt | Rec 70-03 EN 300422 |  |  |  |
| 5- ISL | Yes | Individual license Details in Annex 5 | Rec 70-03 Annex 10 | Radiomics |  | No |
| 6- FIN | 31.100, 32.100, 32.900, 33.500, 36.700, 37.100 MHz, and range 42.400 - 43.600 MHz | License exempt Details in Annex 6 | ERP ≤10 mW; B ≤ 200 kHz. EN 300422 | radio microphones and equipment for in-ear monitoring | - Military use in the band 30.325 - 34.325 MHz; PMSE share use with wireless loudspeakers, headphones, hearing aids, and helmet radio telephones (only frequencies 31.100, 32.100, 32.900, 33.500, 36.700, and 37.100 MHz) - 42.400 - 43.600 MHz shared use with other SRD applications. Usage in other bands includes PMR, control, alarm, telemetry, tele command, data transmission, military use, and SRD applications. | Less use in the future due to lack of equipment |
| 7- DNK | 32 – 39.4 MHz | License exempt Details in Annex 7 | 32.000, 32.400, 35.800, 36.200, 36.500, 36.700, 36.900, 37.100, 37.300, 37.500, 37.700, 37.900, 38.800, 39.000 and 39.400 kHz, BW 50 kHz, 10 mW e.r.p. | radiomics | SRD (ERC/REC 70-03 Annex 8 and 10) | No |
| 8- CZE | 36.4-38.5 MHz | License exempt Details in Annex 8 | 36.4 – 36.65 : 10 mW erp,50 kHz 36.65-38: 2mW, 50 kHz 38-38.5: 10mW, 200kHz | Radiomics in conformity with ERC/REC 70-03 and Commission Decision 2006/771/EU |  | possible extension of sub-bands designated for wireless microphones |
| 9- SUI | A: 31.4 - 31.6 MHz, B: 32.4 - 32.6 MHz, C: 36.0 - 36.2 MHz, D: 36.6 - 36.8 MHz, E: 37.0 - 37.2 MHz, F: 37.2 - 37.4 MHz, G: 37.8 - 38.0 MHz, H: 38.4 - 38.6 MHz, I: 38.9 - 39.1 MHz, K: 39.4 - 39.6 MHz | License exempt Details in Annex 9 | non interference / non protection basis | Radiomics | 30-37.5 MHz : ULP medical membrane implants (ULP-MMI) according to ERC/REC 70-03, Annex 12. UWB Applications | No |
| 10- GEO | Yes | License exempt Details in Annex 10 | Rec 70-03 |  |  |  |
| 11- HOL | 36.6-38.8 MHz | License exempt Details in Annex 11 | 10 mW e.r.p., 50 or 200 kHz bandwidth | low power wireless audio links | mobile communications, medical implants, cordless phones, model control (R/C), radio astronomy, paging, meteor scatter, telemetry, meteorological observations, wind profiler | No |
| 12- NOR | 41-43.6 MHz | General license Details in Annex 12 | 10 mW e.r.p. | radiomics | Maritime Mobile, Fixed, Defence | Depends on changes in Rec. 70-03 |
| 13- EST | 37.6-38.6 MHz | License exempt Details in Annex 13 | 10 mW e.r.p.; 50 kHz | radiomics | Simplex-networks of terrestrial mobile service | No |
| 14- BLR | No |  |  |  |  | No |
| 15- TUR | Yes except 30.3-30.5, 32.15-32.45 and 41.015-47 MHz | License exempt Details in Annex 15 | 10 mW e.r.p., 50 kHz channel separation,. | radiomics | Defense systems, P-MP systems | No |
| 16- LTU | 30.01–30.3, 30.5–32.15, 32.45–37.5 MHz | General License Details in Annex 16 | e.r.p. 10 mW, channel spacing 50 kHz | radiomics | SRD, PMR, military tactical communications | No |
| 17- D | 32.475 – 38.125 MHz | Individual License Details in Annex 17 | e.r.p. 50 mW channel centres and spacing, details in Annex 17 | radiomics | PPDR, military, PMR and Model Control |  |
|  | 32.475 – 34.325 and 36.610 – 38.125 MHz | General License Details in Annex 17 | 10 mW e.r.p.; 50 kHz |  |  | Probably increase of the maximum radiated power for general licence |
| 18- F | / |  |  |  |  | No |
| 19- HRV | No |  |  |  |  | / |
| 20- SVK | 27,75 - 27,9 MHz | General License Details in Annex 20 | 25 mW e.r.p. 12.5 kHz spacing | Radiomics (EN 300422-2 or equivalent) |  | Changes not excluded |
|  | 36,4 - 38,5 MHz |  | 20 mW e.r.p. 50/75 kHz spacing |  | Active medical implants in 36,4 - 37.5 MHz, Defence systems in part 38,25 – 38,5 MHz |  |
| 21- SRB | Frequency allocation table under review |
| 22- I | 41-43.6 MHz | License exempt Details in Annex 22 | Rec 70-03 A10a | radiomics according to Annex 10 of ERC/REC 70-03 | / | No |
| 23- S | 41-43.6 MHz | License exempt Details in Annex 23 | Channel separation 200kHz and max 100 mW e.r.p. | radiomics | / | No |
| 24- HNG | 34.9-38.5 MHz | License exempt Details in Annex 24 | REC 70-03 Annex 10 (ver. June 2009) | radiomics | On site paging applications. SRDs. meteor scatter links. Radio astronomy | No |
| 25- AUT | 36.7; 37.1; 44.55; 45.0 MHz | General License Details in Annex 25 | Details in Annex 25 | No type restrictions | / | No |
| 26- BUL | Yes | License exempt Details in Annex 26 | REC 70-03/Annex 10 | Radiomics | PMR | No |
| 27- G | No |  |  |  |  |  |
| 28- RUS | No |  |  |  |  |  |
| 29- IRL | Yes | License exempt Details in Annex 29 | Details in Annex 29. NIB/NPB | Radio Microphones, In-Ear Monitoring Systems. | SRD’s, Amateur, Amateur-Satellite, Fixed (Government Services), Mobile (Government Services), Paging (Hospitals), Radiolocation (Secondary) | No |
| 30- MLT | in the bands 29.7– 34.9 and 37.5 – 40.98 MHz | General License Details in Annex 30 | Details in Annex 30. NIB/NPB. | Radio microphones | Short range devices | No |
| 31- E | frequency range 31,500-38,550 MHz | License exempt Details in Annex 31 | Max erp 50mW. NIB/NPB | Radiomics |  | No |
| 32- POR | No |  |  |  | Non-specific SRD, Model Control, Inductive applications and Active Medical Implants and their associated peripherals | No |
| 33- GRC | Yes | License exempt Details in Annex 33 | REC 70-03 | Radio microphones | Fixed and Mobile Service for Governmental use , other SRD applications | No |
| 34- LVA | Yes | General License Details in Annex 34 | 10 mW e.r.p., channel spacing 50 kHz | Radio microphones | SRD, defence systems; PMR, ISM | No |

Preliminary analysis

The summary shows that this band, fully or part of it, is widely available for PMSE applications across CEPT (27 from the 32 providing a response on this band). This is mostly for wireless microphones, sometimes with the extension to other low power audio applications. In most of cases, PMSE operation is under license exempt or general licensing regime. A few countries request individual licences, one as a general rule for radiomicrophones, another to allow for more relaxed technical conditions. Concerning the technical conditions, the vast majority follows the provisions from Recommendation 70-03.

2 Band 53-60 MHz

| Annex - Country | Band available? | Licensing regime | Technical conditions | PMSE type | Other use | Change expected? |
| --- | --- | --- | --- | --- | --- | --- |
| 1- MNE | No |  |  |  |  | No |
| 2-CYP | No |  |  |  |  |  |
| 3- LUX | No |  |  |  |  |  |
| 4- MKD | No |  |  |  |  | No |
| 5- ISL | No |  |  |  |  |  |
| 6- FIN | No |  |  |  | Band under review | No |
| 7- DNK | No |  |  |  |  | No |
| 8- CZE | No |  |  |  |  |  |
| 9- SUI | No |  |  |  |  | No |
| 10- GEO | No info |
| 11- HOL | No |  |  |  |  | No |
| 12- NOR | No |  |  |  |  | No |
| 13- EST | No |  |  |  | PMR/PAMR | No |
| 14- BLR | 58 MHz | License exempt Details in Annex 14 | e.r.p. max:25 mW | radiomics | / | No |
| 15- TUR | No |  |  |  |  |  |
| 16- LTU | No |  |  |  |  | No |
| 17- D | No |  |  |  |  | / |
| 18- F | / |  |  |  |  |  |
| 19- HRV | No |  |  |  |  | / |
| 20- SVK | No |  |  |  |  | / |
| 21- SRB | Frequency allocation table under review |
| 22- I | No |  |  |  |  | / |
| 23- S | No |  |  |  |  |  |
| 24- HNG | No |  |  |  |  | No |
| 25- AUT | No |  |  |  | Broadcasting, Land mobile service | No |
| 26- BUL | No |  |  |  |  |  |
| 27- G | 53.75 – 55.75 MHz | Individual license Details in Annex 27 | Maximum in-band ERP 5 W | technology neutral but typically used for fixed audio links | Land mobile | No |
| 28- RUS | No |  |  |  |  |  |
| 29- IRL | No |  |  |  | Amateur (Secondary), Radiolocation (Secondary), SRD’s | No |
| 30- MLT | No |  |  |  | PMR | No |
| 31- E | No |  |  |  |  | No |
| 32- POR | No |  |  |  | Military use; information not available | No |
| 33- GRC | No |  |  |  |  | No |
| 34- LVA | No |  |  |  |  | No |

Preliminary analysis

From the 31 countries providing a response on this band, only 2 of them indicated an availability of part of it for PMSE, one for radio microphones, one typically used for fixed audio links.  The level of harmonisation of this band is thus very low for PMSE.

3 Band 174 – 216 MHz (Rec 70-03 and 25-10)

| Annex - Country | Band available ? | Licensing regime | Technical conditions | PMSE type | Other use | Change expected ? |
| --- | --- | --- | --- | --- | --- | --- |
| 1- MNE | Yes | Individual license Details, see Annex 1 | Rec 70-03 Annex 10 Rec 25-10 (tuning range) | Radiomics | SRD-Assistive Listening Devices, DVB-T2 and T-DAB | No |
| 2-CYP | Yes | Review on a case by case basis |  | Radiomics |  |  |
| 3- LUX | Yes | License exempt Details in Annex 3 | REC 70-03 A10d | Radiomics | UWB, material sensing, aids for hearing, GPR/WPR, BMA | No |
| 4- MKD | Yes | License exempt | Rec 70-03 EN 300422 |  |  |  |
| 5- ISL | Yes | General license |  | Radiomics |  | No |
| 6- FIN | Yes (2ndary basis) | Individual license Details in Annex 6 | Max ERP 50 mW EN300422 | radio microphones and in-ear-monitoring | Broadcasting | No |
| 7- DNK | No |  |  |  | Systems for hearing-impaired Details in Annex 7 | No |
| 8- CZE | Yes | License exempt Details in Annex 8 | 50 mW erp | Radiomics in conformity with ERC/REC 70-03 and Commission Decision 2006/771/EU |  | No |
| 9- SUI | Yes | Individual until 31/12/12 Details in Annex 9 | non interference / non protection basis | Radiomics | DVB-T, T-DAB, Medical Telemetry, Personal hearing aids, UWB. | License exempt by 01.01.2013 for all transmit power levels up to 50 mW |
|  |  | License exempt after 01/01/13 Details in Annex 9 | transmit power levels of 1 to 50 mW: Individual license required until 31.12.2012 |  |  |  |
| 10- GEO | No info |
| 11- HOL | 186.582–188, 202–202.5, 205.4–206.6, 208.2–209, 209 – 216 MHz | Individual license Details in Annex 11 | 10W e.r.p. 200 kHz BW on 10- meters height max. Secondary basis, sharing with other PMSE on equal basis. | wireless audio links, portable or mobile | T-DAB, medical telemetry | Possible extension of frequency bands for PMSE is considered. |
|  | 195 - 202 MHz | License exempt Details in Annex 11 | 50 mW e.r.p., 200 kHz | radiomics |  |  |
| 12- NOR | No |  |  |  |  | Not related to PMSE |
| 13- EST | Yes | License exempt Details in Annex 13 | 50 mW e.r.p | radiomics | DVB-T, T-DAB | No |
| 14- BLR | 144-230 MHz (excluding 148-151, 162.7-163, 168.5-174 MHz) | License exempt Details in Annex 14 | e.r.p. max:20 mW | radiomics | / | No |
| 15- TUR | Yes | License exempt Details in Annex 15 | 50 mW e.r.p. | radiomics | Terrestrial Broadcasting | No |
| 16- LTU | Yes | Light License Details in Annex 16 | e.r.p. 50 mW, | radiomics | TV broadcasting | No |
| 17- D | 174-230 MHz | Individual License Details in Annex 17 | 50 mW e.r.p. BW:200 kHz Raster: 25 kHz | radiomics | Broadcast, hearing aids | No for the time being |
| 18- F | 174-223 MHz | General license Details in Annex 18 | Restricted to professional users, Secondary to broadcasting Details in Annex 18 | SAB ( analogue radiomics, in-ear systems, talk back) | Digital radio | No |
| 19- HRV | Yes | Individual License Details in Annex 19 | Secondary use. Sharing conditions cooperated with other users | equipment according to REC 70-03 | broadcasting services (DVB-T/T2, T-DAB) and Radiodetermination | Electronic licensing in preparation and expected in 2013. |
| 20- SVK | 174.3 174.7 MHz | Light License Details in Annex 20 | 20 mW e.r.p. 50/75 kHz spacing. NI/NPB to broadcasting | Radiomics (EN 300422-2 or equivalent) | ATV Broadcasting in same part 174,260 – 174,740 MHz. and in the future planned service DVB-T and T-DAB | No |
| 21- SRB | Frequency allocation table under review |
| 22- I | 174-216 | General license Details in Annex 22 | according to band d) of Annex 10 of ERC/REC 70-03 | Radiomics |  | No |
|  | 173.965-174.015 | License exempt Details in Annex 20 |  | Hearing aids |  |  |
| 23- S | 174-230 MHz | Individual license Details in Annex 23 | Max BW 200kHz and max 50 mW e.r.p. Use of white spaces | wireless audio | T-DAB and DVB-T/T2 | No |
| 24- HNG | 174-216 MHz | License exempt Details in Annex 24 | REC 70-03 Annex 10 (ver. June 2009) | radiomics | Broadcasting | No |
|  | 190-214 MHz | Individual license Details in Annex 24 | ERPmax= 10 W Operation on a secondary basis | Transmission of television news |  |  |
|  | 214-223 MHz |  |  | Transmission of radio news |  |  |
| 25- AUT | Yes | Individual license Details in Annex 25 | Details in Annex 25 | No type restrictions | / | No |
| 26- BUL | Yes | License exempt Details in Annex 26 | REC 70-03/Annex 10 | Radiomics | Broadcasting | No |
| 27- G | 175.15-175.35, 175.425-175.625, 176.3-177.1, 181.69375-181.80625*, 184.5-185.1, 189.69375-189.80625*, 191.6-193.1**, 199.6-201.1, 207.6-210.1 MHz | Individual license Details in Annex 27 | Maximum in-band ERP 50 mW mic, 25 W talkback, 1 W audio link | technology neutral but typically used for: - wireless microphones -* Talkback - **Audio link | Land and maritime mobile | No |
|  | 12 channels available for microphone use under a shared licence regime. (3 other channels available in mainland UK ie not available in Northern Ireland) | Light license Details in Annex 27 | 50 mW ERP | Microphones |  |  |
| 28- RUS | Yes | License exempt Details in Annex 28 | transmit power max 5mW, antenna gain max 3dB, channel separation – 200 kHz, comply with standard EN 300 422, not claim interference protection | radiomics | broadcasting | Yes |
| 29- IRL | Yes | Individual license for temporary use Details in Annex 29 | Maximum permitted ERP: 1W (although typical licensed ERP is 50 mW) Channel Spacing: 200 kHz Temporary licences are issued on a non-interference, non-protected basis for the duration of the event in question, for a maximum duration of 6 months | Radio Microphones. | Broadcasting (Television). Broadcasting (T-DAB), SRD’s. | No |
| 30- MLT | 173.7 – 181 MHz | General License Details in Annex 30 | Details in Annex 30. Non interference, non protection basis. | Radio microphones | Digital Terrestrial Broadcasting | allocation of radio microphones in this band is temporary |
| 31- E | Yes | License exempt Details in Annex 31 | Max erp 50mW. NIB/NPB | Radiomics | / | No |
|  |  | Individual license Details in Annex 31 | Specific frequencies. Details in Annex 31 | SAB/SAP portable audio links with license |  |  |
| 32- POR | Yes | License exempt Details in Annex 32 | Rec 70-03, max erp 50mW | In-ear monitors and wireless microphones | Broadcasting, Hearing aid equipment | No |
|  |  | Light license Details in Annex 32 | Erp > 50mW Avoid broadcasting emissions |  |  |  |
|  |  | Individual license Details in Annex 32 | Erp > 50mW Temporary basis |  |  |  |
| 33- GRC | Yes | License exempt Details in Annex 33 | Tuning range basis. Max eirp 10mW. NIB | wireless microphones and in-ear systems | Broadcasting | Transitional regulations due to the switch from analogue to digital TV |
|  |  | Individual license Details in Annex 33 | EIRP>10mW Details in Annex 33 |  |  |  |
| 34- LVA | Yes | Individual license Details in Annex 34 | Details in Annex 34 | radio microphones, SAP/SAB | terrestrial broadcasting, hearing aid equipment | No |

Preliminary analysis

From the 32 countries providing a response on this band, 30 of them report about the availability of the band or parts of it for PMSE applications.

The predominant use is for radio microphones (including hearing aids) with technical conditions based in most cases on REC 70-03. However, some countries apply more stringent conditions (lower ERP or requirement on the bandwidth or channel spacing).

The use of this band for radio microphones is generally regulated through license exempt or general license regime, but light or individual licensing may also apply in some countries.

This band is also used for other PMSE applications such as wireless audio links and talkbacks.

4 Band 470 – 786 MHz (Rec 70-03 and 25-10)

| Annex - Country | Band available? | Licensing regime | Technical conditions | PMSE type | Other use | Change expected? |
| --- | --- | --- | --- | --- | --- | --- |
| 1- MNE | Yes | Individual license Details, see Annex 1 | Rec 70-03 Annex 10 Rec 25-10 (tuning range) | Radiomic (tuning range), in-ear monitors | Analogue TV/DVB-T2, and Radio Astronomy(608-614MHz) | No |
| 2-CYP | Yes | Review on a case by case basis |  | Radiomics |  |  |
| 3- LUX | Yes | License exempt Details in Annex 3 | REC 70-03 A10e1 | Radiomics SAB/SAP | GPR/WPR, BMA, material sensing, UWB | No |
| 4- MKD | Yes | License exempt | Rec 70-03 EN 300422 |  |  |  |
| 5- ISL | Yes | General license |  | Radiomics |  | No |
| 6- FIN | Yes (2ndary basis) | Individual license Details in Annex 6 | Max ERP 50 mW EN300422 | radiomics and in-ear-monitoring | Broadcasting | Final decision on future use of the 700 MHz band, and its schedule, has not been made yet. |
| 7- DNK | Yes (in TV white spaces) | License exempt Details in Annex 7 | 50 mW e.r.p., BW 200 kHz + conditions in Annex 7 | radiomics |  | No |
| 8- CZE | Yes | License exempt Details in Annex 8 | 50 mW erp | Radiomics in conformity with ERC/REC 70-03 and Commission Decision 2006/771/EU |  | On the basis of RR 5.296 (WRC-12), operation of the wireless microphones and PMSE on a secondary service. |
| 9- SUI | Yes | Individual until 31/12/12 Details in Annex 9 | non interference / non protection basis | Radiomics, in-ear-monitoring | DVB-T, UWB Applications. | License exempt by 01.01.2013 for all transmit power levels up to 50 mW License exempt by 01.01.2013 for all transmit power levels up to 250 mW in designated frequency ranges |
|  |  | License exempt after 01/01/13 Details in Annex 9 | transmit power levels of 1 to 50 mW: levels up to 250 mW in designated frequency ranges |  |  |  |
|  | 470-782 MHz | Individual license Details in Annex 9 | some frequency ranges, until 5 W transmit power Details in Annex 9 non interference / non protection basis Geographical restrictions in 608-614 | Wireless audio applications |  |  |
| 10- GEO | Yes | License exempt Details in Annex 10 | Rec 70-03 |  |  |  |
| 11- HOL | 470-557 614-637 638-701 702-786 MHz | License exempt Details in Annex 11 | 50 mW e.r.p., 200 kHz | Radiomics | DVB-T, radio astronomy | Preparations for changes / extensions of PMSE in this band. |
|  | 557-618 619-626 627-630 637-638 701-702 MHz | Individual license Details in Annex 11 | 10W e.r.p. 200 kHz BW on 10- meters height max. Secondary basis, sharing with other PMSE on equal basis. | wireless audio links, portable or mobile |  |  |
| 12- NOR | 510-786 | General license Details in Annex 12 | Vacant frequencies 50 mW e.r.p. | radiomics | Digital television broadcast | Possible deployment of white space and cognitive devices in the long term. Also depends on allocation changes and other international harmonisation measures |
| 13- EST | Yes | License exempt Details in Annex 13 | 50 mW e.r.p.; | radiomics | DVB-T | Under consideration |
| 14- BLR | 470-638 MHz | License exempt Details in Annex 14 | e.r.p. max:5 mW | radiomics | / | No |
| 15- TUR | Yes | License exempt Details in Annex 15 | 50 mW e.r.p. | Radiomics and SAB/SAP | Terrestrial Broadcasting | No |
| 16- LTU | Yes | Light License Details in Annex 16 | e.r.p. 50 mW, | radiomics | TV broadcasting | No |
| 17- D | 470 MHz - 606 MHz / 614 MHz -790 MHz | Individual License Details in Annex 17 | 50 mW e.r.p. BW:200 kHz Raster: 25 kHz | Radiomics, | Broadcast, Wind Profiler, Radio Astronomy, Military | No for the time being |
|  | 470 MHz - 790 MHz |  | 30 W erp 20 kHz | SAB/SAP engineering / telecommand |  |  |
|  | 470 MHz - 790 MHz |  | 250 W erp 300 kHz | SAB/SAP P-P |  |  |
| 18- F | yes | General License Details in Annex 18 | Restricted to professional users, Secondary to broadcasting Details in Annex 18 | SAB(radio microphones, in-ear systems, talk back) | Digital TV | New conditions to be published soon |
| 19- HRV | Yes | Individual License Details in Annex 19 | Secondary use. Sharing conditions cooperated with other users | equipment according to REC 70-03 | broadcasting services (DVB-T/T2) and Radiodetermination | Electronic licensing in preparation and expected in 2013 |
| 20- SVK | Yes | Light License Details in Annex 20 | Case by case consideration. NI/NPB to broadcasting | Radiomics | Broadcasting | No |
| 21- SRB | Frequency allocation table under review |
| 22- I | Yes | General license Details in Annex 22 | according to band e1) of Annex 10 of ERC/REC 70-03 | Radiomics for professional use |  | No |
| 23- S | Yes | Individual license Details in Annex 23 | Max BW 200kHz and max 50 mW e.r.p. Use of white spaces | wireless audio | DVB-T/T2 | Outcome of the next WRC (agenda item 1.2) may have an impact |
| 24- HNG | Yes | License exempt Details in Annex 24 | REC 70-03 Annex 10 (ver. June 2009) | radiomics | Broadcasting, Radio astronomy | Yes |
|  |  | Individual license Details in Annex 24 | ERPmax= 10 W Operation on a secondary basis | Transmission of television news |  |  |
|  |  |  |  | Transmission of radio news |  |  |
| 25- AUT | Yes | Individual license Details in Annex 25 | Details in Annex 25 | No type restrictions | BROADCASTING, Radio Astronomy and Radiolocation Service | Regulation will be amended according to ECC REC 70-03 for the full range 470-862 MHz |
| 26- BUL | Yes | License exempt Details in Annex 26 | 50 mW e.r.p. Tuning range basis | Radiomics | Broadcasting – TV, DVB-T, Radionavigation | No |
| 27- G | 470-790 MHz | Individual license Details in Annex 27 | Maximum in-band ERP 50 mW mic and IEM, 5 W talkback | technology neutral but typically used for: microphones, in ear monitors and talkback | TV broadcasting | International developments at WRC-12 with respect to the 700 MHz band raises questions for the future use of UHF Band IV and V in the UK including PMSE. |
|  | 606-614 MHz | Light license Details in Annex 27 | 50 mW ERP | Microphones |  |  |
| 28- RUS | Yes | License exempt Details in Annex 28 | transmit power max 5mW, antenna gain max 3dB, channel separation – 200 kHz, comply with standard EN 300 422, not claim interference protection | radiomics | BROADCASTING, MOBILE, FIXED, SPACE OPERATION | Yes |
|  |  | Individual license Details in Annex 28 | on primary basis, detailed conditions should be defined in licence as result of expertize | Temporary use for major events, limited to residents |  |  |
| 29- IRL | Yes | Individual license for temporary use Details in Annex 29 | Typical licensed ERP: 50 mW Max. Licensed ERP: 1 W Max Channel Bandwidth: 200kHz Temporary licences are issued on a non-interference, non-protected basis for the duration of the event in question, for a maximum duration of 6 months. | Wireless Microphone/In-ear Monitors. | Broadcasting (Television). | No within the next 3 years |
| 30- MLT | No |  |  |  |  | Yes |
| 31- E | No |  |  |  |  | Under study availability in TV white spaces from 2013 |
| 32- POR | 470-750 MHz and 758-786 MHz | License exempt Details in Annex 32 | Rec 70-03, max erp 50mW | In-ear monitors and wireless microphones | Broadcasting, Hearing aid equipment | No |
|  |  | Light license Details in Annex 32 | Erp > 50mW Avoid broadcasting emissions |  |  |  |
|  |  | Individual license Details in Annex 32 | Erp > 50mW Temporary basis |  |  |  |
| 33- GRC | Yes | License exempt Details in Annex 33 | Tuning range basis. Max eirp 10mW. NIB | wireless microphones and in-ear systems | Broadcasting | Transitional regulations due to the switch from analogue to digital TV |
|  |  | Individual license Details in Annex 33 | EIRP>10mW Details in Annex 33 |  |  |  |
| 34- LVA | Yes | Individual license Details in Annex 34 | Details in Annex 34 | radio microphones, SAP/SAB | TV broadcasting, | License regime under consideration |

Preliminary analysis

From the 33 countries providing a response on this band, 31 of them report about the availability of the band or parts of it for PMSE applications.

The predominant use is for radio microphones (and also in-ear monitors) with technical conditions based in most cases on REC 70-03. The use of this band for radio microphones is generally regulated through license exempt or general license regime, but light or individual licensing may and also in-ear monitors also apply in some countries.

This band is also used in some countries for other PMSE applications such as temporary SAB/SAP, talkbacks, wireless audio links generally with higher ERP and in most cases with individual licensing.

A number of countries refer to some international developments on the 700 MHz band (results of WRC-12, WRC-15 AI 1.2, cognitive devices in the white spaces) which may have an impact on PMSE in this band. In addition, the regulation is expected to be amended in some countries to reflect the modifications recently brought to the REC 70-03 in the full range 470-862 MHz.

5 Band 786 – 789 MHz (Rec 70-03 and 25-10)

| Annex - Country | Band available? | Licensing regime | Technical conditions | PMSE type | Other use | Change expected? |
| --- | --- | --- | --- | --- | --- | --- |
| 1- MNE | Yes | Individual license Details, see Annex 1 | Rec 70-03 Annex 10 Rec 25-10 (tuning range) | Radiomic (tuning range), in-ear monitors | Defence systems, Analogue TV/DVB-T2 | No |
| 2-CYP | Yes | Review on a case by case basis |  | Radiomics |  |  |
| 3- LUX | Yes | License exempt Details in Annex 3 | REC 70-03 A10e2 | Radiomics SAB/SAP | GPR/WPR, BMA, material sensing, UWB | No |
| 4- MKD | Yes | License exempt | Rec 70-03 EN 300422 |  |  |  |
| 5- ISL | Yes | General license |  | Radiomics |  | No |
| 6- FIN | Yes (2ndary basis) | Individual license Details in Annex 6 | Max ERP 12 mW EN300422 | radio microphones and in-ear-monitoring | Broadcasting | Final decision on future use of the 700 MHz band, and its schedule, has not been made yet. |
| 7- DNK | Yes (in TV white spaces) | License exempt Details in Annex 7 | 50 mW e.r.p., BW 200 kHz + conditions in Annex 7 | radiomics |  | No |
| 8- CZE | Yes | License exempt Details in Annex 8 | 12 mW erp | Radiomics in conformity with ERC/REC 70-03 and Commission Decision 2006/771/EU |  | No |
| 9- SUI | Yes | Individual until 31/12/12 Details in Annex 9 | transmit power levels of 1 to 50 mW non interference / non protection basis | Radiomics, in-ear-monitoring | DVB-T until 31.12.2012, UWB Applications. | License exempt by 01.01.2013 for all transmit power levels up to 12 mW |
|  |  | License exempt after 01/01/13 Details in Annex 9 | transmit power levels of 1 to 12 mW: |  |  |  |
| 10-GEO | Yes | License exempt Details in Annex 10 | Rec 70-03 |  |  |  |
| 11- HOL | Yes | License exempt Details in Annex 11 | 50 mW e.r.p., 200 kHz | Radiomics | DVB-T | Preparations for changes / extensions of PMSE in this band. |
| 12-NOR | Yes | General license Details in Annex 12 | Vacant frequencies 50 mW e.r.p. | radiomics | Digital television broadcast | Possible deployment of white space and cognitive devices in the long term. Also depends on allocation changes and other international harmonisation measures |
| 13- EST | Yes | License exempt Details in Annex 13 | 12 mW e.r.p.; | radiomics | DVB-T | No |
| 14- BLR | No |  |  |  |  | No |
| 15- TUR | Yes | License exempt Details in Annex 15 | 50 mW e.r.p. | Radiomics and SAB/SAP | Terrestrial Broadcasting | No |
| 16- LTU | Yes | Light License Details in Annex 16 | e.r.p. 50 mW, | radiomics | TV broadcasting | No |
| 17- D | 786-790 MHz | Individual License Details in Annex 17 | 50 mW e.r.p. BW:200 kHz Raster: 25 kHz | Radiomics, | Broadcast, Military | No for the time being |
|  |  |  | 30 W erp 20 kHz | SAB/SAP engineering / telecommand |  |  |
|  |  |  | 250 W erp 300 kHz | SAB/SAP P-P |  |  |
| 18- F | No |  |  |  |  | No |
| 19- HRV | Yes | Individual License Details in Annex 19 | Secondary use. Sharing conditions cooperated with other users | equipment according to REC 70-03 | broadcasting services (DVB-T/T2) and Radiodetermination | Electronic licensing in preparation and expected in 2013 |
| 20- SVK | Yes | Light License Details in Annex 20 | Case by case consideration. NI/NPB to broadcasting | Radiomics | Broadcasting | No |
| 21- SRB | Frequency allocation table under review |
| 22- I | Yes | General license Details in Annex 22 | according to band e2) of Annex 10 of ERC/REC 70-03 | Radiomics for professional use |  | No |
| 23- S | Yes | Individual license Details in Annex 23 | Max BW 200kHz and max 50 mW e.r.p. Use of white spaces | wireless audio | DVB-T/T2 | Outcome of the next WRC (agenda item 1.2) may have an impact |
| 24-HNG | Yes | License exempt Details in Annex 24 | REC 70-03 Annex 10 (ver. June 2009) | radiomics | Broadcasting, | The regulation will be reconsidered after the digital switchover. Individual licensing will be required. |
|  |  | Individual license Details in Annex 24 | ERPmax= 10 W Operation on a secondary basis | Transmission of television news |  |  |
|  |  |  |  | Transmission of radio news |  |  |
| 25- AUT | Yes | Individual license Details in Annex 25 | Details in Annex 25 | No type restrictions | BROADCASTING, | Regulation will be amended according to ECC REC 70-03 for the full range 470-862 MHz |
| 26- BUL | Yes | License exempt Details in Annex 26 | 50 mW e.r.p. Tuning range basis | Radiomics | Broadcasting – TV, DVB-T, Radionavigation | No |
| 27- G | 470-790 MHz | Individual license Details in Annex 27 | Maximum in-band ERP 50 mW mic and IEM, 5 W talkback | technology neutral but typically used for: microphones, in ear monitors and talkback | TV broadcasting | International developments at WRC-12 with respect to the 700 MHz band raises questions for the future use of UHF Band IV and V in the UK including PMSE. |
| 28- RUS | Yes | Individual license Details in Annex 28 | on primary basis, detailed conditions should be defined in licence as result of expertize | Temporary use for major events, limited to residents | BROADCASTING, AERONAUTICAL RADIONAVIGATION | No |
| 29- IRL | Yes | Individual license for temporary use Details in Annex 29 | Typical licensed ERP: 50 mW Max. Licensed ERP: 1 W Max Channel Bandwidth: 200kHz Temporary licences are issued on a non-interference, non-protected basis for the duration of the event in question, for a maximum duration of 6 months. | Wireless Microphone/In-ear Monitors. | Broadcasting (Television). | Not in this specific sub-band |
| 30- MLT | No |  |  |  | Digital Terrestrial Television | No |
| 31- E | No |  |  |  |  | Under study availability in TV white spaces from 2013 |
| 32- POR | Yes | License exempt Details in Annex 32 | Rec 70-03, max erp 50mW | In-ear monitors and wireless microphones | Broadcasting, Hearing aid equipment | No |
|  |  | Light license Details in Annex 32 | Erp > 50mW Avoid broadcasting emissions |  |  |  |
|  |  | Individual license Details in Annex 32 | Erp > 50mW Temporary basis |  |  |  |
| 33- GRC | Yes | License exempt Details in Annex 33 | Tuning range basis. Max eirp 10mW. NIB | wireless microphones and in-ear systems | Broadcasting | Transitional regulations due to the switch from analogue to digital TV |
|  |  | Individual license Details in Annex 33 | EIRP>10mW Details in Annex 33 |  |  |  |
| 34- LVA | Yes | Individual license Details in Annex 34 | Details in Annex 34 | radio microphones, SAP/SAB | TV broadcasting, | use of PMSE devices within 786 – 862 MHz will be aligned to ERC/REC 70-03. License regime under consideration |

Preliminary analysis

From the 33 countries providing a response on this band, 29 of them report about the availability of the band for PMSE applications.

The predominant use is for radio microphones (and also in-ear monitors) with technical conditions based in most cases on REC 70-03 and ECC/DEC(09)03. However, a number of countries apply slightly different conditions, for the maximum ERP level, which are based on previous versions of REC 70-03.

The use of this band for radio microphones is generally regulated through license exempt or general license regime, but light or individual licensing may and also in-ear monitors also apply in some countries.

This band is also used in a few countries for other PMSE applications such as temporary SAB, wireless audio links generally with higher ERP and individual licensing.

In some countries, the regulation is expected to be amended to be in line with the latest version of REC 70-03. In addition, it is stated that some international developments (results of WRC-12, WRC-15 AI 1.2, cognitive devices in the white spaces) may have an impact on PMSE in this band.

6 Band 823-826 MHz (Rec 70-03 and 25-10)

| Annex - Country | Band available? | Licensing regime | Technical conditions | PMSE type | Other use | Change expected? |
| --- | --- | --- | --- | --- | --- | --- |
| 1- MNE | Yes | Individual license Details, see Annex 1 | Rec 70-03 Annex 10 Rec 25-10 (tuning range) | Radiomic (tuning range), in-ear monitors | Analogue TV/DVB-T2, defence systems and mobile service | No |
| 2-CYP | Yes | Review on a case by case basis |  | Radiomics, SAB/SAP |  |  |
| 3- LUX | Yes | License exempt Details in Annex 3 | REC 70-03 A10e3 | Radiomics | None | No |
| 4- MKD | Yes | License exempt | Rec 70-03 EN 300422 |  |  |  |
| 5- ISL | Yes | General license |  | Radiomics |  | No |
| 6- FIN | Yes | License exempt Details in Annex 6 | Max ERP 12 mW 60 mW for bodyworn B ≤ 200 kHz. EN300422 | radio microphones and in-ear-monitoring | 821-823 MHz guard band for ECN | No |
| 7- DNK | Yes (in TV white spaces) | License exempt Details in Annex 7 | Handheld 10 mW e.r.p., Bodyworn 50 mW e.r.p., BW 200 kHz | radiomics |  | No |
| 8- CZE | Yes | License exempt Details in Annex 8 | 20 mW 50 mW for bodyworn B ≤ 200 kHz | Radiomics in conformity with ERC/REC 70-03 and Commission Decision 2006/771/EU |  | No |
| 9- SUI | Yes | Individual until 31/12/12 Details in Annex 9 | transmit power levels of 1 to 50 mW non interference / non protection basis | Radiomics, in-ear-monitoring | DVB-T until 31.12.2012, UWB Applications. | License exemption after 01.01.2013 |
|  |  | License exempt after 01/01/13 Details in Annex 9 | transmit power levels up to 20 mW EIRP (100 mW EIRP bodyworn) |  |  |  |
| 10- GEO | Yes | License exempt Details in Annex 10 | Rec 70-03 |  |  |  |
| 11- HOL | Yes | License exempt Details in Annex 11 | 50 mW e.r.p., 200 kHz | Radiomics | DVB-T is being migrated to <790 MHz | No |
| 12- NOR | Yes | General license Details in Annex 12 | 50 mW e.r.p. | radiomics | None | No |
| 13- EST | Yes | License exempt Details in Annex 13 | 20 mW e.i.r.p., 200 kHz | radiomics | Mobile | No |
| 14- BLR | No |  |  |  |  | No |
| 15- TUR | No |  |  |  |  | No |
| 16- LTU | Yes | Light License Details in Annex 16 | e.r.p. 50 mW, | radiomics | TRA-ECS | No |
| 17- D | Yes | General license Details in Annex 17 | 50 mW e.r.p. BW:200 kHz Raster: 25 kHz | radiomics |  | No for the time being |
| 18- F | Yes | General license Details in Annex 18 | Restricted to professional users, Details in Annex 18 | SAB(radio microphones, in-ear systems, talk back) |  | New conditions to be published soon |
| 19- HRV | Yes | Individual License Details in Annex 19 | Secondary use. Sharing conditions cooperated with other users | equipment according to REC 70-03 | IMT, broadcasting services (DVB-T/T2) and Radiodetermination | Electronic licensing in preparation and expected in 2013 |
| 20- SVK | No |  |  |  |  | / |
| 21- SRB | Frequency allocation table under review |
| 22- I | Yes | General license Details in Annex 22 | according to band e3) of Annex 10 of ERC/REC 70-03 | Radiomics for professional use | / | / |
| 23- S | Yes | License exempt Details in Annex 23 | Max BW 200kHz and max 10 mW e.r.p. handheld or 50 mW e.r.p.bodyworn | wireless audio |  | No |
| 24- HNG | Yes | License exempt Details in Annex 24 | REC 70-03 Annex 10 (ver. June 2009) | radiomics | Broadcasting, | Individual licensing will be required. |
|  |  | Individual license Details in Annex 24 | ERPmax= 10 W Operation on a secondary basis | Transmission of television news |  |  |
|  |  |  |  | Transmission of radio news |  |  |
| 25- AUT | Yes | Individual license Details in Annex 25 | Details in Annex 25 | No type restrictions | Until end of October 2013 the band 822-830 MHz is temporary allocated to the BROADCASTING Service | Regulation will be amended according to ECC REC 70-03 for the full range 470-862 MHz |
| 26- BUL | Yes | License exempt Details in Annex 26 | 50 mW e.r.p. Tuning range basis | Radiomics | Broadcasting – TV, DVB-T, Radionavigation | No |
| 27- G | This band makes up part of the duplex gap and will not be available |  | No |
| 28- RUS | Yes | Individual license Details in Annex 28 | on primary basis, detailed conditions should be defined in licence as result of expertize | Temporary use for major events, limited to residents | BROADCASTING, AERONAUTICAL RADIONAVIGATION | No |
| 29- IRL | Yes | Individual license for temporary use Details in Annex 29 | Typical licensed ERP: 50 mW Max. Licensed ERP: 1 W Max Channel Bandwidth: 200kHz Temporary licences are issued on a non-interference, non-protected basis for the duration of the event in question, for a maximum duration of 6 months. | Wireless Microphone/In-ear Monitors. | Broadcasting (Television). | it is intended to require PMSE users to comply with ECC Decision 09(03) |
| 30- MLT | No |  |  |  |  | This band could be designated for PMSE applications |
| 31- E | No |  |  |  |  | Foreseen availability from 2013 for wireless microphones and SAP/SAB audio links |
| 32- POR | No |  |  |  |  | Under study |
| 33- GRC | Yes | License exempt Details in Annex 33 | Tuning range basis. Max eirp 10mW. NIB | wireless microphones and in-ear systems | Broadcasting | Transitional regulations due to the switch from analogue to digital TV |
|  |  | Individual license Details in Annex 33 | EIRP>10mW Details in Annex 33 |  |  |  |
| 34- LVA | Yes | Individual license Details in Annex 34 | Details in Annex 34 | radio microphones, SAP/SAB | TV broadcasting, | use of PMSE devices within 786 – 862 MHz will be aligned to ERC/REC 70-03. License regime under consideration |

Preliminary analysis

From the 33 countries providing a response on this band, 26 of them report about the current availability of the band for PMSE applications. The availability of the band is also under consideration in 3 other countries.

The predominant use is for radio microphones (and also in-ear monitors) with technical conditions based in most cases on REC 70-03 and ECC/DEC(09)03. However, some countries apply slightly different conditions (presumably based on previous versions of REC 70-03).

The use of this band for radio microphones is generally regulated through license exempt or general license regime, but light or individual licensing may and also in-ear monitors also apply in some countries.

This band is also used in a few countries for other PMSE applications such as temporary SAB, generally with higher ERP and individual licensing.

In some countries, the regulation is expected to be amended to be in line with the latest version of REC 70-03.

7 Band 826-832 MHz (Rec 70-03 and 25-10)

| Annex - Country | Band available? | Licensing regime | Technical conditions | PMSE type | Other use | Change expected? |
| --- | --- | --- | --- | --- | --- | --- |
| 1- MNE | Yes | Individual license Details, see Annex 1 | Rec 70-03 Annex 10 Rec 25-10 (tuning range) | Radiomic (tuning range), in-ear monitors | Analogue TV/DVB-T2, defence systems and mobile service | No |
| 2-CYP | Yes | Review on a case by case basis |  | Radiomics, SAB/SAP |  |  |
| 3- LUX | Yes | License exempt Details in Annex 3 | REC 70-03 A10e4 | Radiomics | None | No |
| 4- MKD | Yes | License exempt | Rec 70-03 EN 300422 |  |  |  |
| 5- ISL | Yes | General license |  | Radiomics |  | No |
| 6- FIN | Yes | License exempt Details in Annex 6 | Max ERP 60 mW B ≤ 200 kHz. EN300422 | radio microphones and in-ear-monitoring | ECN above 832 MHz | No |
| 7- DNK | 826-831 | License exempt Details in Annex 7 | 50 mW e.r.p., BW 200 kHz | radiomics |  | No |
| 8- CZE | Yes | License exempt Details in Annex 8 | 100 mW erp B ≤ 200 kHz | Radiomics in conformity with ERC/REC 70-03 and Commission Decision 2006/771/EU |  | No |
| 9- SUI | Yes | Individual until 31/12/12 Details in Annex 9 | transmit power levels of 1 to 50 mW e.r.p. or to 100 mW e.i.r.p. non interference / non protection basis | Radiomics, in-ear-monitoring | DVB-T until 31.12.2012, UWB Applications. | License exemption after 01.01.2013 |
|  |  | License exempt after 01/01/13 Details in Annex 9 |  |  |  |  |
| 10- GEO | Yes | License exempt Details in Annex 10 | Rec 70-03 |  |  |  |
| 11- HOL | Yes | License exempt Details in Annex 11 | 50 mW e.r.p., 200 kHz | Radiomics | DVB-T is being migrated to <790 MHz | No |
| 12- NOR | Yes | General license Details in Annex 12 | 50 mW e.r.p. | radiomics | None | No |
| 13- EST | Yes | License exempt Details in Annex 13 | 100 mW e.i.r.p., 200 kHz | radiomics | Mobile | No |
| 14- BLR | No |  |  |  |  | No |
| 15- TUR | No |  |  |  |  | No |
| 16- LTU | Yes | Light License Details in Annex 16 | e.r.p. 50 mW, | radiomics | TRA-ECS | No |
| 17- D | Yes | General license Details in Annex 17 | 50 mW e.r.p. BW:200 kHz Raster: 25 kHz | radiomics |  | No for the time being |
| 18- F | 826-830 | General license Details in Annex 18 | Restricted to professional users, Details in Annex 18 | SAB(radio microphones, in-ear systems, talk back) |  | New conditions to be published soon |
| 19- HRV | Yes | Individual License Details in Annex 19 | Secondary use. Sharing conditions cooperated with other users | equipment according to REC 70-03 | IMT, broadcasting services (DVB-T/T2) and Radiodetermination | Electronic licensing in preparation and expected in 2013 |
| 20- SVK | No |  |  |  |  | / |
| 21- SRB | Frequency allocation table under review |
| 22- I | Yes | General license Details in Annex 22 | according to band e4) of Annex 10 of ERC/REC 70-03 | Radiomics for professional use | / | / |
| 23- S | Yes | License exempt Details in Annex 23 | Max BW 200kHz and max 50 mW e.r.p. | wireless audio |  | No |
| 24- HNG | 826-832 MHz | License exempt Details in Annex 24 | REC 70-03 Annex 10 (ver. June 2009) | radiomics | Broadcasting, | Individual licensing will be required. |
|  | 826-830 MHz | Individual license Details in Annex 24 | ERPmax= 10 W Operation on a secondary basis | Transmission of television news |  |  |
|  |  |  |  | Transmission of radio news |  |  |
| 25- AUT | Yes | Individual license Details in Annex 25 | Details in Annex 25 | No type restrictions | Until end of October 2013 the band 822-830 MHz is temporary allocated to the BROADCASTING Service | Regulation will be amended according to ECC REC 70-03 for the full range 470-862 MHz |
| 26- BUL | Yes | License exempt Details in Annex 26 | 50 mW e.r.p. Tuning range basis | Radiomics | Broadcasting – TV, DVB-T, Radionavigation | No |
| 27- G | This band makes up part of the duplex gap and will not be available |  | No |
| 28- RUS | Yes | Individual license Details in Annex 28 | on primary basis, detailed conditions should be defined in licence as result of expertize | Temporary use for major events, limited to residents | BROADCASTING, AERONAUTICAL RADIONAVIGATION | No |
| 29- IRL | Yes | Individual license for temporary use Details in Annex 29 | Typical licensed ERP: 50 mW Max. Licensed ERP: 1 W Max Channel Bandwidth: 200kHz Temporary licences are issued on a non-interference, non-protected basis for the duration of the event in question, for a maximum duration of 6 months. | Wireless Microphone/In-ear Monitors. | Broadcasting (Television). | it is intended to require PMSE users to comply with ECC Decision 09(03) |
| 30- MLT | No |  |  |  | Digital Terrestrial Television | PMSE could be considered if digital terrestrial television is migrated to another channel |
| 31- E | No |  |  |  |  | Foreseen availability from 2013 for wireless microphones and SAP/SAB audio links |
| 32- POR | No |  |  |  |  | Under study |
| 33- GRC | Yes | License exempt Details in Annex 33 | Tuning range basis. Max eirp 10mW. NIB | wireless microphones and in-ear systems | Broadcasting | Transitional regulations due to the switch from analogue to digital TV |
|  |  | Individual license Details in Annex 33 | EIRP>10mW Details in Annex 33 |  |  |  |
| 34- LVA | Yes | Individual license Details in Annex 34 | Details in Annex 34 | radio microphones, SAP/SAB | TV broadcasting, | use of PMSE devices within 786 – 862 MHz will be aligned to ERC/REC 70-03. License regime under consideration |

Preliminary analysis

From the 33 countries providing a response on this band, 26 of them report about the availability of the band or parts of it for PMSE applications. The availability of the band is also under consideration in 3 other countries.

The predominant use is for radio microphones (and also in-ear monitors) with technical conditions based in most cases on REC 70-03 and ECC/DEC(09)03. However, some countries apply more stringent conditions (lower ERP).

The use of this band for radio microphones is generally regulated through license exempt or general license regime, but light or individual licensing may also apply in some countries.

This band is also used in a few countries for other PMSE applications such as temporary SAB, generally with higher ERP and individual licensing.

In some countries, the regulation is expected to be amended to be in line with the latest version of REC 70-03.

8 Band 863 – 865 MHz (Rec 70-03 and 25-10)

| Annex - Country | Band available? | Licensing regime | Technical conditions | PMSE type | Other use | Change expected? |
| --- | --- | --- | --- | --- | --- | --- |
| 1- MNE | Yes | License exempt Website Details in Annex 1 | Rec 70-03 Annex 10 Rec 25-10 (tuning range) | Radiomic | Defence systems, SRD- Non-specific, SRD- Wireless Audio Applications | No |
| 2-CYP | Yes | License exempt Details in Annex 2 | Rec 70-03 Ver 30/05/07 | Radiomics |  |  |
| 3- LUX | Yes | License exempt Details in Annex 3 | REC 70-03 A10c | Radiomics | GPR/WPR, BMA, material sensing, UWB, alarms, social alarms | No |
| 4- MKD | Yes | License exempt | Rec 70-03 EN 300357 |  |  |  |
| 5- ISL | Yes | General license |  | Radiomics |  | No |
| 6- FIN | Yes | License exempt Details in Annex 6 | Max ERP 10 mW B ≤ 200 kHz. EN300422 | radio microphones and in-ear-monitoring (also wireless loudspeakers, headphones, hearing aids, and helmet radio telephones) | SRD applications | No |
| 7- DNK | Yes | License exempt Details in Annex 7 | 10 mW e.r.p. For radiomics: BW 200 kHz. For audio transmission BW no restriction | radiomics or audio transmission |  | No |
| 8- CZE | Yes | License exempt Details in Annex 8 | 10 mW erp | Radiomics in conformity with ERC/REC 70-03 and Commission Decision 2006/771/EU |  | No |
| 9- SUI | Yes | License exempt Details in Annex 9 | 10 mW NIB / NPB | Radiomics, Wireless audio applications according to ERC/REC 70-03 Annex 13 | UWB Applications | No |
| 10- GEO | No info |
| 11- HOL | Yes | License exempt Details in Annex 11 | 10 mW e.r.p. | Radiomics | telemetry ,alarms, data | No |
| 12- NOR | Yes | General license Details in Annex 12 | 10 mW e.r.p. EN301357 | Wireless audio | Non-specific short range devices | No |
| 13- EST | Yes | License exempt Details in Annex 13 | 10 mW e.r.p. | radiomics | SRD | No |
|  |  | Individual license Details in Annex 13 | See Annex 13 | SAB/SAP |  |  |
| 14- BLR | 863.6-865 | License exempt Details in Annex 14 | e.r.p. max:10 mW, spacing 50 kHz | wireless audiosystems | / | No |
| 15- TUR | Yes | License exempt Details in Annex 15 | 10 mW e.r.p. | Radiomics and SAB/SAP |  | No |
| 16- LTU | Yes | General License Details in Annex 16 | e.r.p. 10 mW, | Wireless audio applications, radiomics | SRD, military tactical radio relay | No |
| 17- D | Yes | General license Details in Annex 17 | 10 mW e.r.p. BW:200 kHz for digital, 300 kHz for analogue Raster: 25 kHz | Wireless audio applications | SRD | No for the time being |
| 18- F | Yes | General license Details in Annex 18 | Details in Annex 18 | Wireless audio applications |  | No |
| 19- HRV | Yes | Individual License Details in Annex 19 | Secondary use. Sharing conditions cooperated with other users | equipment according to REC 70-03 | Alarms, SRD, RFID, Wireless audio applications and Radiodetermination | Electronic licensing in preparation and expected in 2013 |
| 20- SVK | Yes | General license Details in Annex 20 | 10 mW e.r.p. 75 kHz spacing EN 300 422-2 or equivalent | Radiomics | Wireless Audio Applications and Non-specific SRD | Changes not excluded |
| 21- SRB | Frequency allocation table under review |
| 22- I | Yes | License exempt Details in Annex 22 | according to band c) of Annex 10 of ERC/REC 70-03 | Radiomics for non-professional use | / | No |
| 23- S | Yes | License exempt Details in Annex 23 | Max BW 200kHz and max 50 mW e.r.p. | wireless audio |  | No |
| 24- HNG | Yes | License exempt Details in Annex 24 | REC 70-03 Annex 10 (ver. June 2009) | Radiomics, | RFIDs, narrow band audio devices, non-specific short range devices | No |
|  |  |  | REC 70-03 Annex 13 (ver. June 2009) | wireless applications |  |  |
| 25- AUT | Yes | General license Details in Annex 25 | Details in Annex 25 | No type restrictions | Wireless audio applications | No |
| 26- BUL | Yes | License exempt Details in Annex 26 | REC 70-03/Annex 10 | Radiomics | Non-specific Short Range Devices, Wireless Audio Applications | No |
| 27- G | Yes | License exempt Details in Annex 27 | Rec 70-03. Details in Annex 27 | Radiomics | / | No |
| 28- RUS | Yes | Individual license Details in Annex 28 | on primary basis, detailed conditions should be defined in licence as result of expertize | Temporary use for major events, limited to residents | AERONAUTICAL RADIONAVIGATION | No |
| 29- IRL | Yes | License exempt Details in Annex 29 | As per ERC Recommendation 70-03. NIB/NPB. | Radiomics | SRDs | No |
| 30- MLT | Yes | General License Details in Annex 30 | Details in Annex 30. NIB/NPB. | Radio microphones | Wireless audio applications | No |
| 31- E | Yes | License exempt Details in Annex 31 | Max e.r.p. 20mW. NIB/NPB | Wireless microphone and audio devices | / | No |
| 32- POR | Yes | License exempt Details in Annex 32 | As defined in Rec 70-03 | Wireless microphones | Non-specific SRDs (863-870 MHz), hearing aid equipment, wireless audio applications | No |
| 33- GRC | Yes | License exempt Details in Annex 33 | REC 70-03 | Radio microphones | Fixed Service for Governmental use , other SRD applications | No |
| 34- LVA | Yes | General License Details in Annex 34 | 10 mW e.r.p. | Radio microphones | SRD | No |

Preliminary analysis

The 32 countries providing a response on this band report about the availability of the band for PMSE applications.

In 31 of these countries, the band is used or planned to be used by radio microphones and also in-ear monitoring and wireless audio applications with technical conditions based in most cases on REC 70-03 (Annex 10 for radio microphones, Annex 13 for wireless audio applications).

The use of this band is generally regulated through license exempt or general license regime, but individual licensing may also apply in a few countries. No change is expected in this band.

9 Band 1785 – 1800 MHz (Rec 70-03 and 25-10)

| Annex - Country | Band available ? | Licensing regime | Technical conditions | PMSE type | Other use | Change expected? |
| --- | --- | --- | --- | --- | --- | --- |
| 1- MNE | Yes | Individual license Details, see Annex 1 | Rec 70-03 Annex 10 Rec 25-10 (tuning range) | Radiomic and in-ear monitors (tuning range) | SRD-Wireless Audio Applications, Mobile Applications | No |
| 2-CYP | 1785.7-1799.4 MHz | License exempt Details in Annex 2 | Rec 70-03 Ver 30/05/07 | Radiomics |  |  |
| 3- LUX | Yes | License exempt Details in Annex 3 | REC 70-03 A10f+g | Radiomics | None | No |
| 4- MKD | Yes | License exempt | Rec 70-03 EN 300422 |  |  |  |
| 5- ISL | Yes | General license |  | Radiomics |  | No |
| 6- FIN | Yes | Individual license Details in Annex 6 | EN 300422 | Radiomic and in-ear monitoring | ECN in adjacent bands | Possible licence-exemption under consideration More use is expected |
| 7- DNK | Yes | License exempt Details in Annex 7 | For radiomics: 20 mW e.r.p., BW 200 kHz. For audio transmission, 20 mW e.i.r.p., BW no restriction | radiomics or audio transmission |  | No |
| 8- CZE | Yes | License exempt Details in Annex 8 | 20 mW 50 mW for bodyworn | Radiomics in conformity with ERC/REC 70-03 and Commission Decision 2006/771/EU |  | No |
| 9- SUI | Yes | License exempt Details in Annex 9 | NIB / NPB | Radiomics | UWB Applications | No |
| 10- GEO | No info |
| 11- HOL | Yes | License exempt Details in Annex 11 | 50 mW e.r.p., 600 kHz | Radiomics | None | No |
| 12- NOR | Yes | General license Details in Annex 12 | 20 mW e.i.r.p. 50 mW e.i.r.p. for bodyworn | radiomics | Defence | No |
| 13- EST | Yes | License exempt Details in Annex 13 | 20 mW e.i.r.p. 50 mW e.i.r.p. for bodyworn | radiomics | SRD | No |
|  |  | Individual license Details in Annex 13 | See Annex 13 | SAB/SAP |  |  |
| 14- BLR | No |  |  |  |  | No |
| 15- TUR | Yes | License exempt Details in Annex 15 | 20 mW e.i.r.p. 50 mW e.i.r.p. for bodyworn | Radiomics and SAB/SAP |  | No |
| 16- LTU | 1785-1795 | Light License Details in Annex 16 | e.r.p. 50 mW, | radiomics |  | No |
|  | 1795-1800 | General License Details in Annex 16 | 20 mW e.i.r.p. 50 mW e.i.r.p. for bodyworn | Wireless audio applications, radiomics |  |  |
| 17- D | 1785-1805 | General license Details in Annex 17 | 50 mW e.r.p. | radiomics | military services, SRD | No for the time being |
| 18- F | Not yet |  |  |  |  | Authorised soon for PMSE professional users under Rec 70-03 conditions |
| 19- HRV | Yes | Individual License Details in Annex 19 | PMSE on a primary basis. Sharing conditions cooperated with other users | equipment according to REC 70-03 | Radiodetermination | Electronic licensing in preparation and expected in 2013 |
| 20- SVK | No |  |  |  |  |  |
| 21- SRB | Frequency allocation table under review |
| 22- I | Planned | No info | according to band g) of Annex 10 of ERC/REC 70-03 | Radiomics | / |  |
| 23- S | Probably in the near future | / | / | / | ‘/ | / |
| 24- HNG | Yes | License exempt Details in Annex 24 | REC 70-03 Annex 10 (ver. June 2009) | Radiomics, | None | No |
|  |  |  | REC 70-03 Annex 13 (ver. June 2009) | wireless applications |  |  |
| 25- AUT | Yes | General license Details in Annex 25 | Details in Annex 25 | No type restrictions | / | / |
| 26- BUL | Yes | License exempt Details in Annex 26 | REC 70-03/Annex 10 | Radiomics Wireless audio applications in 1795-1800 MHz | None | No |
| 27- G | Yes | Individual license Details in Annex 27 | Maximum in-band ERP 50 mW | technology neutral but typically used for wireless microphones | Fixed service | Not at this time |
| 28- RUS | No |  |  |  |  | / |
| 29- IRL | No |  |  |  | WAPECS | No, WAPECS licenses until 2022 |
| 30- MLT | Yes | General License Details in Annex 30 | Details in Annex 30. Non interference, non protection basis. | Radio microphones | Wireless audio applications | No |
| 31- E | Yes | License exempt Details in Annex 31 | Max e.r.p. 20mW. NIB/NPB | Wireless microphone | / | No |
| 32- POR | Yes | License exempt Details in Annex 32 | Rec 70-03, max erp 50mW | In-ear monitors and wireless microphones | Hearing aid equipment, Wireless audio applications | No |
|  |  | Light license Details in Annex 32 | Erp > 50mW Avoid broadcasting emissions |  |  |  |
|  |  | Individual license Details in Annex 32 | Erp > 50mW Temporary basis |  |  |  |
| 33- GRC | Yes | License exempt Details in Annex 33 | REC 70-03 | Radio microphones | Fixed and Mobile Service | No |
| 34- LVA | 1785-1795 MHz | Individuall License. Details in Annex 34 | 20 mW e.i.r.p. ; 50 mW e.i.r.p Details in Annex 34 | digital radio microphones (1785.7 – 1799.4 Mhz) and wireless audio applications (1795 – 1800 MHz) |  | No |
|  | 1795-1800 MHz | General License Details in Annex 34 |  |  |  |  |

Preliminary analysis

From the 32 countries providing a response on this band, 25 of them report about the availability of the band or parts of it for PMSE applications. In addition, 3 countries intend to make the band available in the near future.

The band is used or planned to be used by radio microphones and also in-ear monitoring and wireless audio applications with technical conditions based in most cases on REC 70-03 (Annex 10 for radio microphones, Annex 13 for wireless audio applications).

The use of this band is generally regulated through license exempt or general license regime, but light or individual licensing may also apply in some countries.

It should be noted that one country reported about the availability of the band 1800-1805 MHz under the same conditions than for the 1785-1800 MHz band.

10 Band 2025-2110 MHz (Rec 25-10)

| Annex - Country | Band available? | Licensing regime | Technical conditions | PMSE type | Other use | Change expected? |
| --- | --- | --- | --- | --- | --- | --- |
| 1- MNE | Yes | Individual license Details, see Annex 1 | Rec 25-10 (tuning range), ERC Rep 38 | Cordless cameras, Portable video links, Mobile video links (airborne and vehicular) | Defence systems, Fixed, Space research | No |
| 2-CYP | Yes | Review on a case by case basis |  | SAB/SAP |  |  |
| 3- LUX | No |  |  |  | Military use |  |
| 4- MKD | No |  |  |  |  |  |
| 5- ISL | Yes | Individual license Details in Annex 5 |  | Radio links for mobile TV cameras | Fixed radio links | No |
| 6- FIN | Yes | Individual license Details in Annex 6 | Geographical restrictions or maximum e.i.r.p. level restrictions to protect other services | short term use for wireless cameras and video link. | Few old fixed links and satellite telemetry in co-frequency and IMT in adjacent bands | No |
| 7- DNK | Yes | Individual license Details in Annex 7 | Shared between wireless camera users | ENG/OB, audio links | Satellite Earth Station | No |
| 8- CZE | Yes | Individual license Details in Annex 8 | Coordination with Defence in 2025-2070 | ENG/OB SAB/SAP |  | No |
| 9- SUI | No |  |  |  |  | No |
| 10- GEO | No info |
| 11- HOL | 2070-2110 | Individual License, Details in Annex 11 |  | ENG/OB, temporary use only | mobile | / |
| 12- NOR | 2038,5 and 2052,5 (BW = 14 MHz) | Temporary individual license Details in Annex 12 | Non-exclusive use. Maximum 1 W e.r.p. | Wireless camera | A few Satellite Earth Stations | No |
| 13- EST | 2075.25-2110 MHz | Individual license Details in Annex 13 | See Annex 13 | SAB/SAP | fixed radiolinks; SRD | No |
| 14- BLR | No |  |  |  |  | No |
| 15- TUR | No |  |  |  |  | No |
| 16- LTU | Yes | Individual license for temporary use Details in Annex 16 | e.i.r.p. 6 dBW, 16 dBW and 26 dBW, width of channel 14 MHz. See Annex 16 | Cordless cameras, Portable video links, Mobile video links | Radio relay links | No |
| 17- D | No |  |  |  |  | / |
| 18- F | 2065, 2105MHz, | Individual license Details in Annex 18 | e.i.r.p. max 10 dBW Details in Annex 18 | mobile video links, temporary use (2 months max) Air-ground possible |  | No |
|  | 2055 and 2095 MHz |  | e.i.r.p. max 10 dBW Details in Annex 18 ,Restriction 30 km around Paris | mobile video links, temporary use (2 months max) |  |  |
| 19- HRV | No |  |  |  |  | / |
| 20- SVK | No |  |  |  |  |  |
| 21- SRB | Frequency allocation table under review |
| 22- I | 2040 – 2110 MHz | Individual license Details in Annex 22 | REC 25-10 | SAB/SAP temporary video links, wireless cameras | / | No |
| 23- S | 2025-2045.5, 2094.5-2110 MHz | Individual License Details in Annex 23 | / | temporary mobile video links |  | / |
| 24- HNG | No |  |  |  |  | No |
| 25- AUT | 2070-2110 MHz | Individual license Details in Annex 25 | Details in Annex 25 | No type restrictions (ENG/OB) | / | / |
| 26- BUL | No |  |  |  | Tactical Radiorelay systems for defence | No |
| 27- G | Yes | Individual license Details in Annex 27 | Maximum in-band ERP 20 dBW (13 dBW airborne). Cameras typically licensed at 100 mW ERP | technology neutral but typically used for; wireless cameras/video links. | Defence systems | Not at this time |
| 28- RUS | No |  |  |  |  | / |
| 29- IRL | Yes | Individual license for temporary use Details in Annex 29 | ERP: 1 W Max Channel Bandwidth: 10MHz. Geographical restrictions. Airborne not permitted. Temporary licences are issued on a non-interference, non-protected basis for the duration of the event in question, for a maximum duration of 6 months. | Wireless cameras. | Fixed P-P | No |
| 30- MLT | Yes | Individual License Details in Annex 30 | See Annex 30. | Radio links (studio-to-transmitter) including OB links | / | No |
| 31- E | No |  |  |  |  | No |
| 32- POR | Yes | Individual License for temporary use Details in Annex 32 | No sharing constraints, see Annex 32 | wireless cameras or video links |  | No |
| 33- GRC | Yes | Individual License for temporary use Details in Annex 33 | Defined on case by case basis | wireless cameras, mobile video links | Fixed and Mobile Service | No |
| 34- LVA | No |  |  |  |  | No |

Preliminary analysis

From the 32 countries providing a response on this band, 19 of them report about the availability of the band or parts of it for PMSE applications, namely temporary video links (portable, mobile with some allowance for airborne use) and cordless cameras as referred to in ERC/REC 25-10. This use is under an individual licensing regime. No change is expected for this band in relation to PMSE.

11 Band 2200-2500 MHz (Rec 25-10)

| Annex - Country | Band available? | Licensing regime | Technical conditions | PMSE type | Other use | Change expected? |
| --- | --- | --- | --- | --- | --- | --- |
| 1- MNE | 2200-2290 2300-2400 and 2483,5-2500 MHz | Individual license Details, see Annex 1 | Rec 25-10 (tuning range), ERC Rep 38 | Cordless cameras, Portable video links, Mobile video links (airborne and vehicular) | Defence systems (2200-2290 MHz), Fixed(2200-2290 MHz), Space research(2200-2290 MHz), Continuum line and VLBI observations (2200-2290 MHz), Mobile applications(2300-2400 MHz) , Aeronautical telemetry (2300-2400 MHz), Amateur radio (2300-2400 MHz), ISM(2483,5-2500 MHz), Mobile applications (2483,5-2500 MHz), Mobile satellite applications(2483,5-2500 MHz), IMT Satellite component(2483,5-2500 MHz) | No |
| 2-CYP | 2200-2290 2300-2400 and 2483,5-2500 MHz | Review on a case by case basis |  | SAB/SAP |  |  |
| 3- LUX | 2335-2395 | Individual license Details in Annex 3 | Case by Case analysis Details in Annex 3 | Temporary wireless video | In the band 2400-2483.5MHz: GPR/WPR, BMA, material sensing, UWB, AVI, ISM | parts of the band 2.3-2.4GHz might not be anymore available in future for PMSE. |
| 4- MKD | No |  |  |  |  |  |
| 5- ISL | Yes | Individual license Details in Annex 5 |  | Radio links for mobile TV cameras | Fixed radio links | PMSE out of the band 2300-2400 MHz in few years |
| 6- FIN | 2200-2300 | Individual license Details in Annex 6 | Geographical restrictions or maximum e.i.r.p. level restrictions to protect other services | short term use for wireless cameras and video link. | IMT and RLAN/ISM in the adjacent bands | No |
|  | 2315-2400 | Individual license Details in Annex 6 | Shared between wireless camera users, coordination | Wireless cqmeras and ENG links |  |  |
| 7- DNK | 2200-2290 MHz, 2300-2400 MHz | Individual license Details in Annex 7 | Shared between wireless camera users | ENG/OB, Audio-links, Wireless cameras | Satellite Earth Station | Users in 2300-2400 MHz are migrating to 2200-2290 MHz or 2025-2110 MHz (2300-2400 MHz expected for wireless broadband in the future). |
| 8- CZE | Yes | Individual license Details in Annex 8 | In 2300–2412 MHz, 4 28 MHz channels for short-term SAP/SAB. | SAB/SAP |  | No |
| 9- SUI | 2290-2300 Emergency services mobile TV links | Individual license Details in Annex 9 | Details in Annex 9 | Cordless cameras, ENG and OB applications. Portable digital video link, Airborne video link | Military equipment, Aeronautical telemetry (mil), UWB Applications. | No |
|  | 2300-2400 |  |  |  |  |  |
| 10- GEO | No info |
| 11- HOL | 2245-2495 | Individual License, Details in Annex 11 | 2245-2300: limited to the event 2300-2495: max 1 year, shared with other users | ENG/OB, temporary use only | Mobile (military), mobile (except aeronautical), amateur (satellite), SRD, mobile (satellite) | / |
| 12- NOR | 2327 and 2390 (BW = 8 MHz) | General license Details in Annex 12 | Maximum 2 W e.i.r.p. | Wireless camera | Fixed links, ISM, others. | No |
| 13- EST | 2200 – 2300; 2390 – 2400 MHz | Individual license Details in Annex 13 | See Annex 13 | SAB/SAP | fixed radiolinks; SRD; S – PCS (S – E) | No |
| 14- BLR | No |  |  |  |  | No |
| 15- TUR | No |  |  |  | 2200-2450 MHz fixed links, PMSE can be regarded as fixed links- individual license required | No |
| 16- LTU | Yes | Individual license for temporary use Details in Annex 16 | e.i.r.p. 6 dBW, 16 dBW and 26 dBW, width of channel 14 MHz. See Annex 16 | Cordless cameras, Portable video links, Mobile video links | Radio relay links, P-MP, WLAN, SRD | No |
| 17- D | 2320 – 2350, 2384 – 2483.5 MHz | Individual license Details in Annex 17 | max. 500 W eirp Transmitter output: max 20 W BW: up to 20 MHz Channel raster: 1 MHz . | cordless cameras, video links | SRD, Amateur, PMAR, Military, PPDR | No for the time being |
| 18- F | 2295, 2305 ,2465, 2475 MHz | Individual license Details in Annex 18 | Details in Annex 18 Limited to ground to ground at 2295 MHz | mobile video links, temporary use (2 months max) |  | Potential change for frequency 2305 MHz. Consideration of implementation of MFCN in 2300-2400 MHz through appropriate regulatory framework (LSA). |
| 19- HRV | 2245-2400 MHz | Individual License Details in Annex 19 | Operations on primary basis. Sharing conditions cooperated with other users | equipment according to REC 25-10. For local event. | Space Research/EESS, Radio astronomy Radiodetermination | Electronic licensing in preparation and expected in 2013 |
| 20- SVK | 2300-2400 MHz | Individual license Details in Annex 20 | Case by case consideration. Coordinated frequencies. | SAB/SAP |  | / |
| 21- SRB | Frequency allocation table under review |
| 22- I | 2215 – 2500 MHz | Individual license Details in Annex 22 | REC 25-10 | SAB/SAP temporary video links, wireless cameras | / | No |
| 23- S | 2200-2220.5, 2269.5-2290 and 2301-2400 MHz | Individual License Details in Annex 23 | / | temporary mobile video links |  | / |
| 24- HNG | 2400-2483.5 MHz | License exempt Details in Annex 24 | REC 70-03 Annex 3. (if comprehensible as PMSE) (ver June 2009) | Wideband data transmission | Radioamateur. Non-PMSE SRDs (according to ERC/REC 70-03). Earth stations of satellite radiocommunication systems. | No |
|  |  |  | REC 70-03 Annex 1 (ver. June 2009) | Non-specific Short Range Devices (SRDs for video transmissions) |  |  |
| 25- AUT | 2245-2400 MHz | Individual license Details in Annex 25 | Details in Annex 25 | No type restrictions (ENG/OB) | / | / |
|  | 2400-2483.5 MHz | General license Details in Annex 25 | Details in Annex 25 | No type restrictions (non-specific SRD) | / | / |
| 26- BUL | 2300-2400 MHz | General license Details in Annex 26 | 6 dBW e.i.r.p. for Wireless camera, 16 dBW e.i.r.p. for Portable link, 26 dBW e.i.r.p. for Mobile link | Wireless camera, Portable link, Mobile link | Radio Amateur in 2300-2450 MHz | No |
| 27- G | 2200-2300 2390-2500 MHz | Individual license Details in Annex 27 | Maximum in-band ERP 20 dBW (13 dBW airborne). Cameras typically licensed at 100 mW ERP | technology neutral but typically used for; wireless cameras/video links. | Defence systems. FS at 2450-2500 MHz | Not at this time |
| 28- RUS | Yes | Individual license Details in Annex 28 | on primary basis, detailed conditions should be defined in licence as result of expertize | Temporary use for major events, limited to residents | Mobile, Radiolocation, Space operation (s-s, s-E),Space exploration (s-s, s-E),EESS (s-s, s-E), Fixed | No |
| 29- IRL | 2200-2400 | Individual license for temporary use Details in Annex 29 | MaxBW=10MHz 2200 -2280MHz: Max ERP = 1W.Geographic limitations. Airborne not permitted. 2280 – 2300, 2330-2340, 2350-2400 MHz : Max ERP = 5W. No geographic Limitations. Airborne permitted. 2300 – 2330 MHz: Max ERP = 100 mW. Geographic. Airborne not permitted. 2340 – 2350 MHz: Maximum ERP = 5 W. Available for newsgathering on a shared restricted nationwide basis. Airborne use not permitted. Temporary licences are issued on a non-interference, non-protected basis for the duration of the event in question, for a maximum duration of 6 months. | Wireless cameras. | Fixed Links (Infrastructure), Multi-Access Radio Links. Parliamentary TV coverage. SRD’s. Amateur (Secondary), Satellite Personal Communications Service | 2300 – 2400 MHz may be considered for other broadband applications in the future, which may have an impact upon future PMSE use in the band |
|  | 2400-2483.5 MHz | License exempt Details in Annex 29 | Details in Annex 29. Non-interference, non-protected basis | Video surveillance |  |  |
| 30- MLT | 2200 – 2290 MHz, 2300 – 2400 MHz | Individual license Details in Annex 30 | See Annex 30 | Radio links (studio-to-transmitter) including OB links and wireless cameras | / | No |
|  | 2400 – 2483.5 MHz | License exempt Details in Annex 30 |  |  |  |  |
| 31- E | 2304.5-2480.5 MHz | Individual license Details in Annex 31 | See Annex 31 | ENG/OB video links | / | No |
| 32-POR | 2200-2400 MHz and 2483,5-2500 MHz | Light license Details in Annex 32 | see Annex 32 | wireless cameras or video links |  | No |
|  |  | Individual license Details in Annex 32 | No sharing constraints, see Annex 32 |  |  |  |
| 33- GRC | Yes | Individual License for temporary use Details in Annex 33 | Defined on case by case basis | wireless cameras, mobile video links, temporary P-P video links | Fixed and Mobile Service | No |
| 34- LVA | 2370 – 2400 MHz | Individual license Details in Annex 34 | Details in Annex 34 | SAB/SAP |  | No |

Preliminary analysis

From the 32 countries providing a response on this band, 29 of them report about the availability of the band or parts of it for PMSE applications.

The main type (28 countries) is related to temporary video links (portable, mobile with some allowance for airborne use) and cordless cameras as referred to in ERC/REC 25-10. In most cases, this use is under an individual licensing regime, although low power wireless cameras can in a few countries operate under a general license.

It is noted that, in addition or as an alternative, 2 countries mention specifically the use of the 2400-2483.5 MHz band for wideband data transmissions or non-specific SRD as per REC 70-03 for PMSE purpose.

5 countries mentioned that current considerations on the potential introduction of Broadband Wireless systems in the band 2300-2400 MHz may have an impact on the availability of the band for PMSE.

12 Band 2500-2690 MHz (Rec 25-10)

| Annex - Country | Band available? | Licensing regime | Technical conditions | PMSE type | Other use | Change expected? |
| --- | --- | --- | --- | --- | --- | --- |
| 1- MNE | 2520-2670 MHz | Individual license Details, see Annex 1 | Rec 25-10 (tuning range), ERC Rep 38 | Portable video links, Mobile video links (airborne and vehicular) | Fixed, IMT, Defence systems(2520-2655MHz), Continuum observations (2655-2670MHz) | The band 2500-2690 MHz will not be available for video SAP/SAB links after the introduction of UMTS/IMT-2000. |
| 2-CYP | 2520-2670 MHz | Review on a case by case basis |  | SAB/SAP |  |  |
| 3- LUX | No |  |  |  | MFCN |  |
| 4- MKD | No |  |  |  |  |  |
| 5- ISL | No |  |  |  |  |  |
| 6- FIN | No |  |  |  |  |  |
| 7- DNK | No |  |  |  |  | No |
| 8- CZE | Yes | Individual license Details in Annex 8 | In subbands not used by the assigned networks | SAB/SAP |  | Changes expected as the auction of 2500–2690 MHz spectrum has been announced |
| 9- SUI | No |  |  |  |  | No |
| 10- GEO | No info |
| 11- HOL | No |  |  |  |  |  |
| 12- NOR | No |  |  |  |  | No |
| 13- EST | No |  |  |  | Fixed; Mobile; SRD | No |
| 14- BLR | No |  |  |  |  | No |
| 15- TUR | No |  |  |  |  | No |
| 16- LTU | No |  |  |  |  | No |
| 17- D | No |  |  |  |  | / |
| 18- F | No |  |  |  |  | / |
| 19- HRV | No |  |  |  |  | / |
| 20- SVK | No |  |  |  |  | / |
| 21- SRB | Frequency allocation table under review |
| 22- I | No |  |  |  |  | / |
| 23- S | No |  |  |  |  | / |
| 24- HNG | No |  |  |  |  | No |
| 25- AUT | No |  |  |  | MOBILE and FIXED, assigned to ECS | No |
| 26- BUL | No |  |  |  | National security | / |
| 27- G | Yes | Individual license Details in Annex 27 | Maximum in-band ERP 0 dBW. Cameras typically licensed at 100 mW ERP | technology neutral but typically used for; wireless cameras/video links. | / | The band is to be awarded. PMSE use will have to cease and is subject to three months notice |
| 28- RUS | Yes | Individual license Details in Annex 28 | on primary basis, detailed conditions should be defined in licence as result of expertize | Temporary use for major events, limited to residents | Mobile (except AMS), Radiolocation, BSS, Space exploration (passive),EESS (passive), Radio astronomy, Fixed | No |
| 29- IRL | No |  |  |  | Terrestrial Electronic Communications Services, including MMDS Services Distribution | The 2500 – 2690 MHz band may be released for other services in the future |
| 30- MLT | No |  |  |  | planned for electronic communications services (EC Decision 2008/477/EC) | No |
| 31- E | No |  |  |  |  | No |
| 32- POR | No |  |  |  | Terrestrial Electronic Communications Services | No |
| 33- GRC | No |  |  |  |  | No |
| 34- LVA | No |  |  |  |  | No |

Preliminary analysis

From the 32 countries providing a response on this band, 5 of them report about the availability of the band or parts of it for PMSE application, namely SAB/SAP, video links. Amongst those, 3 countries expect that the use of PMSE will cease because of the introduction of terrestrial Electronic Communications Networks in the 2500-2690 MHz band.

On this basis, the relevance of maintaining this band in the ERC/REC 25-10 may be considered.

13 Band 2700-3400 MHz

| Annex - Country | Band available? | Licensing regime | Technical conditions | PMSE type | Other use | Change expected? |
| --- | --- | --- | --- | --- | --- | --- |
| 1- MNE | No |  |  |  |  | No |
| 2-CYP | No |  |  |  |  |  |
| 3- LUX | No |  |  |  | aeronautical radionavigation (2700-2900MHz) and radiolocation services (2900-3400MHz) |  |
| 4- MKD | No |  |  |  |  |  |
| 5- ISL | No |  |  |  |  |  |
| 6- FIN | No |  |  |  |  |  |
| 7- DNK | No |  |  |  |  | No |
| 8- CZE | No |  |  |  |  |  |
| 9- SUI | No |  |  |  |  | No |
| 10- GEO | No info |
| 11- HOL | No |  |  |  |  |  |
| 12- NOR | No |  |  |  |  | No |
| 13- EST | No |  |  |  | SRD | No |
| 14- BLR | No |  |  |  |  | No |
| 15- TUR | No |  |  |  |  | No |
| 16- LTU | No |  |  |  |  | No |
| 17- D | No |  |  |  |  | / |
| 18- F | No |  |  |  |  | / |
| 19- HRV | No |  |  |  |  | No |
| 20- SVK | No |  |  |  |  | / |
| 21- SRB | Frequency allocation table under review |
| 22- I | No |  |  |  |  | / |
| 23- S | Yes | / | / | temporary use of mobile video links | / | / |
| 24- HNG | No |  |  |  |  | Yes, usage of UWB SRDs for video transmissions is expected |
| 25- AUT | No |  |  |  |  | No |
| 26- BUL | No |  |  |  | Radiodetermination applications, GPR/WPR | No |
| 27- G | No |  |  |  |  |  |
| 28- RUS | No |  |  |  |  | / |
| 29- IRL | No |  |  |  | Radar and Navigation Services, Meteorological Radar, Maritime Radionavigation Service, Radar Beacons (RACON’s), Active Sensors. | No |
| 30- MLT | No |  |  |  | Primarily, equipment used for aeronautical radionavigtion | No |
| 31- E | No |  |  |  |  | No |
| 32-POR | No |  |  |  | Radionavigation and radiolocation equipment | No |
| 33- GRC | No |  |  |  |  | No |
| 34- LVA | No |  |  |  |  | No |

Preliminary analysis

From the 31 countries providing a response on this band, the band 2.7-2.9 GHz is available in one single country for temporary use of mobile video links. None of the 30 countries where this band is not available expect any change with regard to PMSE in this band.

14 Band 3400 – 3600 MHz (Rec. 25-10)

| Annex - Country | Band available? | Licensing regime | Technical conditions | PMSE type | Other use | Change expected? |
| --- | --- | --- | --- | --- | --- | --- |
| 1- MNE | Yes | Individual license Details, see Annex 1 | Rec 25-10 (tuning range), ERC Rep 38 | Mobile video links(airborne and vehicular) for occasional use | BWA,FSS,IMT, Radars(Upper limit for airborne radars is 3410 MHz) | No |
| 2-CYP | No |  |  |  |  |  |
| 3- LUX | No |  |  |  | TRA-ECS (BWA) and FSS earth stations |  |
| 4- MKD | No |  |  |  |  |  |
| 5- ISL | No |  |  |  |  |  |
| 6- FIN | No |  |  |  |  |  |
| 7- DNK | No |  |  |  |  | No |
| 8- CZE | Yes | Individual license Details in Annex 8 | In subbands where FWA is not operated | temporary ENG/OB terrestrial digital links |  | No |
| 9- SUI | Yes (unused part of the band) | Individual and temporary license Details in Annex 9 | SAP/SAB and ENG/OB: Temporary use in frequencies not used for BWA. Cordless cameras, max. 4 W e.i.r.p., | Cordless cameras | Fixed links, BWA, FSS (S/E). UWB Applications. | No |
| 10- GEO | No info |
| 11- HOL | 3410-3500 | Individual License, Details in Annex 11 |  | ENG/OB, temporary use only | Fixed satellite (military), radiolocation (military), amateur, fixed, mobile, radiolocation | / |
| 12- NOR | No |  |  |  |  | No |
| 13- EST | No |  |  |  | Fixed; mobile; SRD | No |
| 14- BLR | No |  |  |  |  | No |
| 15- TUR | No |  |  |  |  | No |
| 16- LTU | No |  |  |  |  | No |
| 17- D | 3410 - 3594 MHz | Individual license Details in Annex 17 | max. 10 W eirp BW: up to 10 MHz Channel raster: 1 MHz coordination with the primary user MFCN in a restricted area . | cordless cameras, video links | MFCN / Fixed | No for the time being |
| 18- F | Parts of it for specific events | Individual license Details in Annex 18 | Details in Annex 18 | mobile video links, temporary use | / | Development of IMT could reduce the spectrum available for video mobile links. Need for studies on access and sharing opportunities to maintain temporary usage for video mobile links in this band |
| 19- HRV | No |  |  |  |  | / |
| 20- SVK | No |  |  |  |  | / |
| 21- SRB | Frequency allocation table under review |
| 22- I | 3500 – 3600 MHz | Individual license Details in Annex 22 | REC 25-10 | SAB/SAP temporary video links, wireless cameras | / | No |
| 23- S | No |  |  |  |  | / |
| 24- HNG | No |  |  |  |  | No |
| 25- AUT | No |  |  |  |  | Assignment to ENG/OB in the band 3494-3510 MHz under consideration (by individual license) |
| 26- BUL | No |  |  |  | BWA 3400-3600, Radioamateur 3400-3500, FSS Space-Earth 3400-3700 MHz | No |
| 27- G | 3400-3440, 3500-3580 MHz | Individual license Details in Annex 27 | Maximum in-band ERP up to 40 dBW. Cameras typically licensed at 100 mW ERP | technology neutral but typically used for; wireless cameras/video links. | Defence systems | The band 3500-3580 has been identified for release (by MOD) in 2015/2016. Possible short term sharing opportunities which increase geographical restrictions on PMSE |
| 28- RUS | Yes | Individual license Details in Annex 28 | on primary basis, detailed conditions should be defined in licence as result of expertize | Temporary use for major events, limited to residents | FS, FSS (s-E), Radiolocation | No |
| 29- IRL | No |  |  |  | Terrestrial Electronic Communications Services, including FWPMA and FWALA, Licence Exempt VSAT Receivers, Radiolocation (Government Services) | No |
| 30- MLT | No |  |  |  | broadband wireless access applications | No |
| 31- E | No |  |  |  |  | No |
| 32- POR | No |  |  |  | FWA/BWA | No |
| 33- GRC | No |  |  |  |  | No |
| 34- LVA | No |  |  |  |  | No |

Preliminary analysis

From the 32 countries providing a response on this band, 9 of them report about the availability of the band or parts of it for PMSE applications, which tends to confirm a decrease of the availability of this band for PMSE.

PMSE applications in this band cover temporary video links (portable, mobile with some allowance for airborne use) and cordless cameras as referred to in ERC/REC 25-10. This use is under an individual licensing regime.

The development of IMT in this band may have an impact on the spectrum available for PMSE in this band.

15 Band 4400 – 5000 MHz

| Annex - Country | Band available? | Licensing regime | Technical conditions | PMSE type | Other use | Change expected? |
| --- | --- | --- | --- | --- | --- | --- |
| 1- MNE | Yes | Individual license Details, see Annex 1 |  | coordinated SAB/SAP applications for occasional use | Defence systems, TLPR(4500-500 MHz),FSS(4500-4800 MHz), Continuum observations and VLBI(4800-5000MHz), Passive sensors (satellite)(4800-4990MHz)BBDR(4940‐4990 MHz) |  |
| 2-CYP | Yes | Review on a case by case basis |  | SAB/SAP |  |  |
| 3- LUX | Yes | General license with notification |  | coordinated SAP/SAB applications for temporary use |  | No |
| 4- MKD | No |  |  |  |  |  |
| 5- ISL | No |  |  |  |  |  |
| 6- FIN | No |  |  |  |  |  |
| 7- DNK | No |  |  |  |  | No |
| 8- CZE | Yes | Individual license Details in Annex 8 |  | Coordinated temporary SAB/SAP links |  | No |
| 9- SUI | No |  |  |  |  | No |
| 10- GEO | No info |
| 11- HOL | Yes | Individual License, Details in Annex 11 |  | ENG/OB, temporary use only | Mobile (miltary), radioastronomy. | / |
| 12- NOR | No |  |  |  |  | No |
| 13- EST | No |  |  |  | Fixed; mobile; SRD | No |
| 14- BLR | No |  |  |  |  | No |
| 15- TUR | No |  |  |  |  | No |
| 16- LTU | No |  |  |  |  | No |
| 17- D | No |  |  |  |  | / |
| 18- F | No |  |  |  |  |  |
| 19- HRV | No |  |  |  |  | / |
| 20- SVK | No |  |  |  |  | / |
| 21- SRB | Frequency allocation table under review |
| 22- I | No |  |  |  |  | / |
| 23- S | 4400-4500, 4990-5000 MHz | Individual License, Details in Annex 23 | Max EIRP, service area limitations etc. | PMSE on a temporary basis | Mil. Use (4400-4800 MHz), FSS downlink (4500-4800 MHz), Mil.use, RAS (4800-4990 MHz), RAS (4990—5000 MHz) | Depends on the outcome of the WAPECS- investigation |
| 24- HNG | No |  |  |  |  | usage of UWB SRDs for video transmissions is expected. |
| 25- AUT | 4400-4516 MHz | Individual License, Details in Annex 25 | Details in Annex 25 | No type restrictions | / | / |
| 26- BUL | No |  |  |  | National security | No |
| 27- G | No |  |  |  | / | / |
| 28- RUS | No |  |  |  |  | / |
| 29- IRL | No |  |  |  | Terrestrial Electronic Communications Services, including FWPMA and FWALA, Licence Exempt VSAT Receivers, Radiolocation (Government Services) | No |
| 30- MLT | No |  |  |  | Short range devices | No |
| 31- E | No |  |  |  |  | No |
| 32- POR | No |  |  |  | Military use; information not available | No |
| 33- GRC | No |  |  |  |  | No |
| 34- LVA | No |  |  |  |  | No |

Preliminary analysis

From the 32 countries providing a response on this band, 7 of them report about the availability of the band or parts of it for PMSE applications.

PMSE applications in this band cover SAB/SAP links for temporary use deployed in a coordinated way to protect other use (mainly military applications). This PMSE use is in most cases under an individual licensing regime.

16 Band 5250 – 5850 MHz

| Annex - Country | Band available? | Licensing regime | Technical conditions | PMSE type | Other use | Change expected? |
| --- | --- | --- | --- | --- | --- | --- |
| 1- MNE | No |  |  |  |  |  |
| 2-CYP | No |  |  |  |  |  |
| 3- LUX | No |  |  |  |  |  |
| 4- MKD | No |  |  |  |  |  |
| 5- ISL | No |  |  |  |  |  |
| 6- FIN | No |  |  |  |  |  |
| 7- DNK | No |  |  |  |  | No |
| 8- CZE | No |  |  |  |  | No |
| 9- SUI | No |  |  |  |  | No |
| 10- GEO | No info |
| 11- HOL | 5725-5850 | Individual License, Details in Annex 11 |  | ENG/OB, temporary use only | EESS, mobile (except aeronautical), radiolocation, space research, maritime radionavigation, amateur | / |
| 12- NOR | No |  |  |  |  | No |
| 13- EST | No |  |  |  | SRD; ARN; BFWA | No |
| 14- BLR |  |  |  |  |  |  |
| 15- TUR | No |  |  |  | 5150-5350 MHz & 5470-5725 MHz are used for wideband data transmission, PMSE can be regarded as wideband data transmission systems | No |
| 16- LTU | No |  |  |  |  | No |
| 17- D | No |  |  |  |  | / |
| 18- F | No |  |  |  |  | / |
| 19- HRV | No |  |  |  |  |  |
| 20- SVK | No |  |  |  |  | / |
| 21- SRB | Frequency allocation table under review |
| 22- I | No |  |  |  |  | / |
| 23- S | No |  |  |  |  |  |
| 24- HNG | 5250-5350, 5470-5725 MHz | License exempt Details in Annex 24 | WAS/RLAN see REC 70-03 Annex 3 (if applicable as PMSE)(ver. June2009) | Wideband data transmission | Different non-PMSE SRDs (according to ERC/REC 70-03), FSS Earth Stations, FS P-P and P-MP links, meteorological radars, radiolocation | No |
|  | 5725-5850 MHz |  | REC 70-03 Annex 1 (ver. June 2009) | Non-specific Short Range Devices (SRDs for video transmissions) |  |  |
| 25- AUT | No |  |  |  |  | No |
| 26- BUL | No |  |  |  | WAS/RLAN 5150-5350 MHz, 5470-5725 MHz; Non-specific SRD 5725-5850 MHz; Radioamateur 5650-5725 MHz; FSS Earth-Space 5725-5850 MHz | No |
| 27- G | 5472-5588, 5682.5-5702.5, 5705-5725, 5732.5-5752.5, 5770-5790, 5795-5815 MHz | Individual license Details in Annex 27 | Maximum in-band ERP up to 40 dBW (23 dBW airborne). Cameras typically licensed at 100 mW ERP | technology neutral but typically used for; wireless cameras/video links. | Defence systems | No |
| 28- RUS | 5250-5350, 5650-5850 MHz | Individual license Details in Annex 28 | on primary basis, detailed conditions should be defined in licence as result of expertize | Temporary use for major events, limited to residents | Mobile (except AMS), Radiolocation, Space exploration, EESS (active), FSS, amateur, amateur satellite | No |
| 29- IRL | No |  |  |  | Fixed-Satellite (E/S), SRD’s, Meteorological Service Radar, Radiolocation (Position Fixing Equipment), Weather Radar, Amateur (Secondary) FSTV, FWA | No |
| 30- MLT | Yes | General license. Details in Annex 30 | See Annex 30 non-interference / non-protection basis |  | Wireless Access Systems and Radiolocation | No |
| 31- E | No |  |  |  |  | / |
| 32- POR | No |  |  |  | Non-specific SRDs, wideband data transmission, road transport and traffic telematics, radiodetermination, radiolocation, amateur, amateur-satellite, FSS, ISM applications | No |
| 33- GRC | No |  |  |  |  | No |
| 34- LVA | No |  |  |  |  | No |

Preliminary analysis

From the 32 countries providing a response on this band, 5 of them report about the availability of the band or parts of it for PMSE applications.

In 3 cases, this use refers to temporary ENG/OB use regulated through individual licenses in specific frequency bands or ranges. Another country mentions specifically the use of bands at 5 GHz for wideband data transmissions (WAS/RLAN) or non-specific SRD as per REC 70-03 (version June 09) for PMSE purpose.

17 Band 10.0 – 10.68 GHz (Rec. 25-10)

| Annex - Country | Band available? | Licensing regime | Technical conditions | PMSE type | Other use | Change expected? |
| --- | --- | --- | --- | --- | --- | --- |
| 1- MNE | Yes | Individual license Details, see Annex 1 | Rec 25-10 (tuning range), ERC Rep 38 | Portable video links (10-10,6 GHz) and Temporary point-to-point video links | Fixed, TLPR ( 10-10,6 GHz), Non civil radar(10-10,15 GHz), Amateur radio (10-10,5 GHz), FWA(10-15-10,3 GHz and 10,5-10,65 GHz), Civil and military radars(10,15-10,5GHz), Continuum and VLBI measurements(10,6-10,68 GHz), Passive sensors (satellite)(10,6-10,68 GHz) | No |
| 2-CYP | Yes | Review on a case by case basis |  | SAB/SAP |  |  |
| 3- LUX | Yes | License exempt | Rec 25-10 | Cordless cameras/portable video links (10.0-10.6GHz), temporary P2P video links (whole band) |  | No |
| 4- MKD | No |  |  |  |  |  |
| 5- ISL | No |  |  |  |  |  |
| 6- FIN | 10-10.15 GHz | Individual license Details in Annex 6 |  | ENG links | Fixed Wireless Access | No |
| 7- DNK | 10.15-10.45 10.5-10.68 GHz | Individual license Details in Annex 7 | To be decided on case by case | ENG/OB, Wireless Cameras (No current use) | Fixed links, FWA, ERC/REC 70-03 Annex 6 | No |
| 8- CZE | 10.3-10.5 | Individual license Details in Annex 8 | REC 25-10 on dedicated channels. | ENG/OB video links |  | No |
|  | 10.420–10.476 GHz and 10.588–10.644 |  | Channel centres at 10 434 MHz, 10 462 MHz, 10 602 MHz and 10 630 MHz. MaxBW 28 MHz. In 10.60–10.68 GHz max e.i.r.p. of +40 dBW and the power delivered to the antenna limited to -3 dBW (RR 5.482) | temporary and local use by the ENG/OB video links |  | No |
| 9- SUI | Yes | Individual and temporary license Details in Annex 9 | max. 4 dBW e.i.r.p. | Cordless cameras, | Amateur radio service, Point to Point fixed links, 10.5 – 10.6 GHz: SRD according to ERC/REC 70-03, UWB Applications | No |
|  |  |  | 10.0 - 10.6 GHz: max. 40 dBW e.i.r.p., 10.6 – 10.68 GHz max -3dBW, | Point-to-Point video links operated at fixed locations, |  |  |
| 10- GEO | No info |
| 11- HOL | No |  |  |  |  |  |
| 12- NOR | No |  |  |  |  | No |
| 13- EST | 10.3-10.45 GHz | Individual license Details in Annex 13 | See Annex 13 | SAB/SAP | fixed radiolinks; SRD; | No |
| 14- BLR | No |  |  |  |  | No |
| 15- TUR | 10.38-10.55 GHz | Individual license See Annex 15 |  | SAB/SAP | Fixed links | No |
| 16- LTU | Yes | Individual license for temporary use Details in Annex 16 | e.i.r.p. 6 dBW, 16 dBW and 26 dBW, width of channel 28 MHz. See Annex 16 | Cordless cameras, Portable video links, Temporary point-to-point video links | Radio relay links, P-MP, Radars, SRD | No |
| 17- D | 10.4-10.68 GHz | Individual license Details in Annex 17 | max. 10 kW eirp BW: up to 56 MHz In 10,6 - 10,68 GHz, maximum radiated power depends on the angle of elevation, ATPC required | cordless cameras, video links | Amateur; EESS, Radio Astronomy | No for the time being |
| 18- F | 10.569 10.579 GHz | Individual license Details in Annex 18 | Details in Annex 18 | mobile video links, temporary use (max 2 months) | / | No |
| 19- HRV | Yes | Individual License Details in Annex 19 | Secondary use. Sharing conditions cooperated with other users | equipment according to REC 25-10. Local event | Amateur, BWA, Detection of movement and alert, Passive sensors (satellite), Radio astronomy and Radiodetermination | Electronic licensing in preparation and expected in 2013 |
| 20- SVK | 10.3-10.5 GHz | Individual License Details in Annex 20 | Case by case consideration. Coordinated frequencies. | P-P analogue and digital links for TV signal transmission | / | / |
| 21- SRB | Frequency allocation table under review |
| 22- I | 10.3–10.45, 10.5 – 10.68 GHz | Individual license Details in Annex 22 | REC 25-10 | SAB/SAP temporary video links, wireless cameras | / | No |
| 23- S | 10.476-10.56 GHz | Individual License, Details in Annex 23 | Max EIRP, service area limitations etc. | Temporary PMSE. Common usage : mobile video link | Mil.use in the band 10450-10550 MHz | No |
| 24- HNG | Yes | Individual License, Details in Annex 24 | Channel spacing tv:28 MHz radio:1.75 MHz Max. antenna feed 10-10.6 GHz: 0 dBW 10.6-10.68 GHz: -3 dBW Min. antenna gain: 30 dBi Max. EIRP: 40 dBW | Radio and television news and programme transmissions | / | No |
|  | 10.434-10.5 GHz | License exempt Details in Annex 24 | EIRPmax = 100 mW | Video applications |  |  |
| 25- AUT | No |  |  |  |  | Allocation to ENG/OB within the band 10.650-10.680 GHz under consideration |
| 26- BUL | 10-10.50 GHz | General license Details in Annex 26 | 6 dBW e.i.r.p. for Wireless camera, 16 dBW e.i.r.p. for Portable link, 40 dBW e.i.r.p. for Mobile link | Wireless camera, Portable link, Temporary P-P link | Fixed service 10,15-10,68 GHz, Radioamateur 10-10,50 GHz | No |
| 27- G | 10.3-10.36 GHz | Individual license Details in Annex 27 | Maximum in-band ERP up to 40 dBW | technology neutral but typically used for video links. | Defence systems | No |
| 28- RUS | YES (in specific sub-bands: 5250 – 5350 MHz and 5650 – 5850 MHz) | Individual license Details in Annex 28 | on primary basis, detailed conditions should be defined in licence as result of expertize | Temporary use for major events, limited to residents | RADIOLOCATION, amateur(10 – 10,55 GHz),fixed (10 – 10,45 GHz; 10,5 – 10,68 GHz), mobile (10 -10,45 GHz, 10,5 – 10,55 GHz, 10,55 – 10,68 GHz(except AMS)), 10,45 -10,5 GHz (mobile satellite), space exploration and satellite Earth exploration (passive) (10,6 – 10,68 GHz) | No |
| 29- IRL | 10.3-10.5 GHz | Individual license for temporary use Details in Annex 29 | ERP: 5 W Max Channel Bandwidth: 10MHz. Geographical restrictions. Airborne use is permitted. Temporary licences are issued on a non-interference, non-protected basis for the duration of the event in question, for a maximum duration of 6 months. | Wireless cameras. | FWALA , Amateur (Secondary), Amateur-Satellite (Secondary), SRD’s | No |
| 30- MLT | 10 – 10.45 GHz and 10.5 – 10.68 GHz | Individual license Details in Annex 30 | Details in Annex 30 | Radio links (studio-to-transmitter) including OB links | Amateur Radio and SRDs | No |
| 31- E | 10.000,5-10.416,5 MHz | Individual license Details in Annex 31 | Details in Annex 31 | ENG/OB video links | / | No |
|  | 10.416,5-10.496,5 MHz | License exempt Details in Annex 31 |  |  |  |  |
| 32- POR | Yes | Light license Details in Annex 32 | see Annex 32 | Video links | Radiodetermination applications, Amateur, Amateur-satellite. | No |
|  |  | Individual license Details in Annex 32 | No sharing constraints, see Annex 32 |  |  |  |
| 33- GRC | Yes | Individual License for temporary use Details in Annex 33 | Defined on case by case basis | wireless cameras, temporary P-P video links | Fixed, Mobile Service, Radiolocation, Radio Astronomy | No |
| 34- LVA | 10-10.15 GHz | Individual license: Details in Annex 34 | Details in Annex 34 | SAP/SAB | Fixed links | No |

Preliminary analysis

From the 32 countries providing a response on this band, 26 of them report about the availability of the band or parts of it for PMSE applications. The amount of available spectrum and the frequency bands within the overall tuning range vary significantly depending upon the country.

The main PMSE applications covered in this range are wireless cameras, portable video links and point-to-point video links for temporary use as referred to in ERC/REC 25-10. This use is in most cases under an individual licensing regime. No major change is generally expected for this band in relation to PMSE.

18 Band 21.20 – 24.50 GHz (Rec. 25-10)

| Annex - Country | Band available? | Licensing regime | Technical conditions | PMSE type | Other use | Change expected? |
| --- | --- | --- | --- | --- | --- | --- |
| 1- MNE | 21.2-23,6 24-24,5 GHz | Individual license Details, see Annex 1 | Rec 25-10 , ERC Rep 38 | Cordless cameras and Temporary point-to-point video links | SRR(21,4-24,45 GHz),Unidirectional temporary fixed or mobile links ((21,2-21.4 GHz) and (22,6-23 GHz)), Passive sensors (satellite)((21,2-21,4) and (22,21-22.5) GHz),BSS (21,4-22 GHz), Wideband High Definition Television(21,4-22 GHz), Radio astronomy ((22-22,21 GHz) and (22,5-23.55 GHz), Fixed(22-23,6 GHz),Amateur radio (24-24,25 GHz),ISM (24-24,25 GHz), Non-Specific SRDs(24-24,25 GHz), Defence systemsc(24,05-24,25 GHz), TLPR (24,05-24,45 GHz) and Unidirectional fixed links (24,25-24,45 GHz) | No |
| 2-CYP | 21.2-21.4 22-23,6 24-24,5 GHz | Review on a case by case basis |  | SAB/SAP |  |  |
| 3- LUX | 21.2-21.4, 22.6-23 GHz. | License exempt | Rec 25-10 | cordless cameras, and temporary P2P video links | ISM, non-specific SRDs, RTTT, UWB, TLPR , material sensing |  |
| 4- MKD | No |  |  |  |  |  |
| 5- ISL | No |  |  |  |  |  |
| 6- FIN | Part available | Individual license Details in Annex 6 |  | ENG links (no current use) |  |  |
| 7- DNK | 21.2-21.4 MHz, 24.25-24.5 MHz | Individual license Details in Annex 7 | To be decided on case by case | ENG/OB, Wireless Cameras (No current use) | Fixed links, FWA, ERC/REC 70-03 Annexes 1 and 6 | No |
| 8- CZE | 22.592–22.704 GHz | Individual license Details in Annex 8 | four channels 22 606 MHz, 22 634 MHz, 22 662 MHz and 22 690 MHz. BW : 28 MHz. REC 25-10, | ENG/OB SAB/SAP |  | No |
|  | 24.25–24.5 GHz |  | digital modulation | temporary fixed links SAP/SAB |  |  |
| 9- SUI | 21.20 - 21.40 GHz 24.25 - 24.50 GHz | Individual license Details in Annex 9 | Max. 20 W EIRP | Cordless cameras, Portable digital video link | 21.4 – 22.0 GHz: Fixed: Various systems. 24.25 - 24.5 GHz: Automotive SRR | No |
|  | 21.40 - 22.00 GHz 24.25 - 24.50 GHz |  | Max. 100 kW EIRP | Point-to-Point video links operated at fixed locations |  |  |
| 10- GEO | No info |
| 11- HOL | 21.2-21.4 22.6-23 GHz | Individual License, Details in Annex 11 |  | ENG/OB, temporary use only | fixed, BSS, mobile, radioastronomy, EESS, space research, amateur, amateur (satellite), radiolocation | / |
| 12- NOR | No |  |  |  |  | No |
| 13- EST | 21.2-21.4 GHz | Individual license Details in Annex 13 | See Annex 13 | SAB/SAP | fixed radiolinks; SRD; | No |
| 14- BLR | No |  |  |  |  | No |
| 15- TUR | 22-23.6 GHz | Individual license See Annex 15 |  | SAB/SAP | Fixed links | No |
| 16- LTU | 21.2-21.4, 22.6-23.0, 24.25-24.5 GHz | Individual license for temporary use Details in Annex 16 | e.i.r.p. 13 dBW and 40 dBW, width of channel 14 MHz. See Annex 16 | Cordless cameras, Temporary point-to-point video links | Radio relay links, SRR | No |
| 17- D | 21.4-22 GHz | Individual license Details in Annex 17 | max. 1000 W eirp max. 100 mW transmit power, BW: up to 56 MHz | mobile point to point video links | / | No for the time being |
| 18- F | 21413,21441, 21469,21497, 21525,21553, 21581,21805, 21833,21861, 21889,21917, 21945,21073, 22716.75, 22744.75, 22968.75 22996.75 MHz | Individual license Details in Annex 18 | 28 MHz channels Details in Annex 18 | Fixed video links, temporary use (max 2 months) | / | No |
|  | 22709.75, 22723.75, 22737.75, 22751.75, 22961.75, 22975.75, 22989.75, 23003.75 MHz |  | 14 MHz channels Details in Annex 18 |  |  |  |
|  | 24.255-24.445 GHz |  | Details in Annex 18 | Mobile video links, temporary use (max 2 months) |  |  |
| 19- HRV | 21.2-21.4, 24-24.5 GHz | Individual License Details in Annex 19 | Secondary use. Sharing conditions cooperated with other users | equipment according to REC 25-10. Local event | Passive sensors (satellite), | Electronic licensing in preparation and expected in 2013 |
| 20- SVK | 21.2-21.4 GHz | Individual License Details in Annex 20 | Case by case consideration. Coordinated frequencies. | Mobile SAB/SAP ENG/OB |  |  |
| 21- SRB | Frequency allocation table under review |
| 22- I | 21.20– 21.40, 22.7680 – 23.0 GHz | Individual license Details in Annex 22 | REC 25-10 | SAB/SAP | / | No |
| 23- S | 21.4-22.0 GHz is available for occasional use via satellite, but currently not used. | / | / | / | / | Depends on the on-going work within ITU-R on the Harmonization of ENG/OB-bands |
| 24- HNG | 21.2–21.4, 22.6–23 GHz | Individual License, Details in Annex 24 | Channel spacing tv:28 MHz radio:1.75 MHz Max antenna feed: 0 dBW Min. antenna gain: 30 dBi Max. EIRP: 40 dBW | Radio and television news and programme transmissions | Fixed digital radio links, radio astronomy and space research, EESS, various non-PMSE SRDs. Amateur service | The use of cordless cameras will be permitted |
|  | 24-24.25 GHz | License exempt Details in Annex 24 | REC 70-03 Annex 1 (ver. June 2009) EIRPmax = 100 mW | Non-specific Short Range Devices (video transmissions) |  |  |
| 25- AUT | No |  |  |  |  | Allocation to ENG/OB within the band 22.600-23.000 GHz under consideration |
| 26- BUL | 21.2-21.4 GHz | General license Details in Annex 26 | 13 dBW e.i.r.p. for Wireless camera, 40 dBW e.i.r.p. for Temporary point-to-point link | Wireless camera, Temporary point-to-point link | Fixed service 21,2-23,6 GHz, Radioamateur 24-24,25GHz | No |
| 27- G | 24.25-24.5 GHz | Individual license Details in Annex 27 | Maximum in-band ERP up to 40 dBW | technology neutral but typically used for video links. | Fixed service | No |
| 28- RUS | No |  |  |  |  | / |
| 29- IRL | 24-24.25 GHz | License exempt Details in Annex 29 | Details in Annex 29 | Wireless CCTV. | SRD’s, Fixed Links (Infrastructure), Radioastronomy, Amateur, Amateur-Satellite | No |
| 30- MLT | 21.2 – 21.4, 22.6 – 23 and 24.25 – 25 GHz | Individual license Details in Annex 30 | See Annex 30 | Point-to-point video links (temporary use) | SRDs | No |
| 31- E | 21.2 – 21.4 GHz | Individual license Details in Annex 31 | See Annex 31 | ENG/OB video links | / | No |
| 32- POR | No |  |  |  | Non-specific SRDs, ISM, Road transport, and traffic telematics, Radiodetermination applications, Fixed links, Short range radars, Amateur, Amateur-satellite. | No |
| 33- GRC | Yes | Individual License for temporary use Details in Annex 33 | Defined on case by case basis | wireless cameras, temporary P-P video links | Fixed Service, | No |
| 34- LVA | 21.2–21.4; 22.6-23; 24.25-24.5 GHz | Individual license: Details in Annex 34 | Details in Annex 34 | SAP/SAB | Fixed links, SRR | No |

Preliminary analysis

From the 32 countries providing a response on this band, 25 of them report about the availability of the band or parts of it for PMSE applications. The amount of available spectrum and the frequency bands within the overall tuning range vary significantly depending upon the country.

The main PMSE applications covered in this range are wireless cameras, portable video links and point-to-point video links for temporary use as referred to in ERC/REC 25-10. This use is in most cases under an individual licensing regime. A few changes are expected, which may slightly increase the availability of spectrum for PMSE.

19 Band 47.20 -  50.20 GHz (Rec. 25-10)

| Annex - Country | Band available? | Licensing regime | Technical conditions | PMSE type | Other use | Change expected? |
| --- | --- | --- | --- | --- | --- | --- |
| 1- MNE | Yes | Individual license Details, see Annex 1 | Rec 25-10 , ERC Rep 38 | Cordless cameras | FSS, Feeder links(47,2-48,54 GHz), Fixed(48,2-50,2 GHz), and Radio astronomy (48,54-49,44 GHz) | No |
| 2-CYP | Yes | Review on a case by case basis |  | SAB/SAP |  |  |
| 3- LUX | No |  |  |  |  |  |
| 4- MKD | No |  |  |  |  |  |
| 5- ISL | No |  |  |  |  |  |
| 6- FIN | Part available No use | Individual license Details in Annex 6 |  | ENG links |  |  |
| 7- DNK | 48.2-48.54 GHz | Individual license Details in Annex 7 | To be decided on case by case | ENG/OB, Wireless Cameras (No current use) | Fixed links, FWA, ERC/REC 70-03 Annex 6 | No |
| 8- CZE | Yes | Individual license Details in Annex 8 | Rec 25-10. | Wireless cameras |  | No |
| 9- SUI | Yes | Individual license Details in Annex 9 | max. 20 W e.i.r.p. | Cordless cameras, Portable video link. | High Altitude Platform Stations (HAPS) in the bands: 47.2-47.5 GHz / 47.9-48.2 GHz. | No |
| 10- GEO | No info |
| 11- HOL | Yes | Individual License, Details in Annex 11 | / | / | mobile | / |
| 12- NOR | No |  |  |  |  | No |
| 13- EST | 47.2-48.5 GHz | Individual license Details in Annex 13 | See Annex 13 | SAB/SAP | No | No |
| 14- BLR | No |  |  |  | No |  |
| 15- TUR | No |  |  |  | No |  |
| 16- LTU | Yes | Individual license for temporary use Details in Annex 16 | e.i.r.p. 13 dBW, width of channel 14 MHz and 28 MHz. See Annex 16 | Cordless cameras, | / | No |
| 17- D | No |  |  |  |  | / |
| 18- F | No |  |  |  |  |  |
| 19- HRV | Yes | Individual License Details in Annex 19 | Secondary use. Sharing conditions cooperated with other users | equipment according to REC 25-10. Local event | FSS Earth stations, High Density FSS, Point-to-Point, Radio astronomy | Electronic licensing in preparation and expected in 2013 |
| 20- SVK | No |  |  |  |  |  |
| 21- SRB | Frequency allocation table under review |
| 22- I | No |  |  |  |  |  |
| 23- S | No |  |  |  |  | / |
| 24- HNG | Yes | License exempt Details in Annex 24 | EIRPmax =13 dBW Min TX antenna gain = 0 dBi Min RX antenna gain = 6 dBi | Cordless cameras | HDFSS, P-P radio links, radio astronomy service | No |
| 25- AUT | No |  |  |  |  | No |
| 26- BUL | 47.2-48.5 GHz | General license Details in Annex 26 | 13 dBW e.i.r.p. | Wireless camera | FSS (Space-Earth, Earth-Space) 47,2-50,2 GHz, Radioamateur 47,2-47,9 GHz, 48,2-48,54 GHz | No |
| 27- G | 48-48.40 GHz | Individual license Details in Annex 27 | Maximum in-band ERP up to 30 dBW | technology neutral but typically used for video links. | FS, FSS, MS | No |
| 28- RUS | No |  |  |  |  | / |
| 29- IRL | No |  |  |  | None | No |
| 30- MLT | Yes | Individual license Details in Annex 30 | See Annex 30 | Cordless cameras (no current use) | / | No |
| 31- E | No |  |  |  |  | No |
| 32- POR | No |  |  |  | Fixed links | No |
| 33- GRC | Yes | Individual License for temporary use Details in Annex 33 | Defined on case by case basis | wireless cameras | Fixed, Mobile and Fixed Satellite Services | No |
| 34- LVA | 47.2–47.5; 47.5–47.9; 47.9-48.2; 48.2-48.5 GHz | Individual license: Details in Annex 34 | Details in Annex 34 | SAP/SAB |  | No |

Preliminary analysis

From the 32 countries providing a response on this band, 16 of them report about the availability of the band or parts of it for PMSE applications.

The main PMSE applications covered in this range are wireless cameras and portable video links as referred to in ERC/REC 25-10. This use is in most cases under an individual licensing regime. No change is expected with regard to PMSE in this band.

20 Other bands

| Annex - Country | Band | Licensing regime | Technical conditions | PMSE type | Other use | Change expected ? |
| --- | --- | --- | --- | --- | --- | --- |
| 1- MNE | No |  |  |  |  |  |
| 2-CYP | / |  |  |  |  |  |
| 3- LUX | / |  |  |  |  |  |
| 4- MKD | / |  |  |  |  |  |
| 5- ISL | 337-338 MHz | Individual license Details in Annex 5 |  | mobile links for FM Broadcasting stations |  | No |
| 6- FIN | 7900-8500 MHz |  |  |  |  | Intention to reserve few channels according to ECC/REC/(02)06 to transportable digital program delivery links. |
| 7- DNK | 789-790 MHz (in TV white spaces) | License exempt Details in Annex 7 | conditions in Annex 7 | radiomics |  | No |
| 8- CZE | 169-174 MHz | License exempt Details in Annex 8 | Frequency band e.r.p. Channel spacing 169.4–169.475 MHz 500 mW . 50 kHz 169.4875–169.5875 MHz 173.300 MHz 50 mW 75 kHz 173.965–174.015 MHz 2 mW 50 kHz | Radiomics in conformity with ERC/REC 70-03 and Commission Decision 2006/771/EU |  | No |
| 9- SUI | 5850-5925 MHz | Individual license Details in Annex 9 | max. 316 kW e.i.r.p. | SAP/SAB Point-to-Point video links operated at fixed locations. | 5725 - 5795 MHz and 5815 - 5875 MHz: BFWA, 5850 – 5875 MHz: SRDs, .5855 – 5925 MHz: ITS, 5850 – 5925 MHz: FSS VSAT, ISM Band, UWB Applications. | No |
| 10- GEO | / |  |  |  |  |  |
| 11- HOL | 61-68 MHz | Individual License, Details in Annex 11 | / | No known use | Mobile(military) | / |
|  | 216-223 MHz | Individual License, Details in Annex 11 |  | No known use | T-DAB |  |
|  | 789-823 MHz | License exempt Details in Annex 11 | 50 mW e.r.p., 200 kHz | Radiomics | DVB-T is being migrated to <790 MHz MCN | usage of 791-821 is allowed to 31/12/15 on NIB/no protection basis, 789-791 MHz and 821-823 remain available for wireless microphones. |
|  | 832-862 MHz | License exempt Details in Annex 11 | 50 mW e.r.p., 200 kHz | Radiomics | DVB-T is being migrated to <790 MHz MCN | Usage is allowed to 31/12/15 on NIB/no protection basis, no available for PMSE after. |
| 12- NOR | 800-820 MHz | General license Details in Annex 12 | 20 mW e.r.p. max | Radiomics | None | Use not permitted after 31/12/13. Band used for mobile broadband |
| 13- EST | No |  |  |  |  |  |
| 14- BLR | 66-74 MHz, 87,5-92 MHz, 100-108 MHz | License exempt Details in Annex 14 | 20 mW e.r.p. max |  |  |  |
| 15- TUR | / |  |  |  |  |  |
| 16- LTU | No |  |  |  |  |  |
| 17- D | / |  |  |  |  |  |
| 18- F | 7110-7250 MHz | Individual License, Details in Annex 18 | Details in Annex 18 | Fixed video links Temporary uses (less than 2 months) |  | No |
|  | 7750-7890 MHz |  | Details in Annex 18 Limited area: 50 km around Paris |  |  |  |
|  | 38 - 39.48 GHz | Individual License, Details in Annex 18 |  | Temporary use |  | No |
| 19- HRV | 3600-3800 MHz | Individual License Details in Annex 19 | Operations on primary basis. Sharing conditions cooperated with other users | equipment according to REC 25-10. For local event. | IMT, Non-specific SRDs and Radiodetermination | Electronic licensing in preparation and expected in 2013 |
| 20- SVK | 149.4 149.475 149.5 149.55 | General License Details in Annex 20 | 25 mW e.r.p. 12.5 kHz spacing | Radiomics | PMR and Telemetry in part 149,393 -149,557 MHz |  |
|  | 7138-7195 MHz |  |  | Mobile SAB/SAP ENG/OB |  |  |
|  | 8550-8700 MHz |  |  | Fixed SAB/SAP |  |  |
| 21- SRB | Frequency allocation table under review |
| 22- I | 216-223 MHz | General License Details in Annex 22 | according to Annex 10 of ERC/REC 70-03 | Radiomics for professional use | / | No |
|  | 789-790 MHz | General License Details in Annex 22 | according to Annex 10 of ERC/REC 70-03 | Radiomics for professional use | / | No |
| 23- S | / | / | / | / | / | / |
| 24- HNG | No other bands assigned explicitly for PMSE use. SRD devices used for PMSE purposes are allowed based on the ERC/REC 70-03 (June 2009) |
| 25- AUT | 230-250 MHz | Individual license Details in Annex 25 | Details in Annex 25 | No type restrictions | / | / |
| 26- BUL | / |  |  |  |  |  |
| 27- G | 47.55-48.8, 52-52.95, 60.75-62.75, 67.75-67.8375, 69.15625-69.18125, 74.68125-74.71875, 75.2625-75.3*, 76.80625-76.84375, 78.18375-78.25875, 82.65625-82.68125, 86.66875-86.68125, 86.80625-86.84375*, 139.54375-139.55625, 139.56875-139.58125, 139.64375-139.66875, 140.9875-141.4875*, 148.5625-148.5875, 148.7125-148.7375 MHz | Individual license Details in Annex 27 | Maximum in-band ERP 25 W (5 W airborne) *Some airborne use permitted | technology neutral but typically used for talkbacks. | Land mobile, Fixed service, Defence systems | No |
|  | 425.3125-425.5625, 427.7625-428.0125, 442.2625-442.5125, 446.425-447.5125, 454.9875-455.475*, 457.25-457.475*, 461.23125-461.25625*, 462.75-463*, 467.2625-469.875* MHz | Individual license Details in Annex 27 | Maximum in-band ERP 25 W (5 W airborne) *Some airborne use permitted | technology neutral but typically used for talkbacks. | Land mobile, Fixed service, Defence systems | No |
|  | 790-862 MHz | Individual license Details in Annex 27 | Maximum in-band ERP 50 mW mic and IEM, 5 W talkback | technology neutral but typically used for: microphones, in ear monitors and talkback | TV broadcasting | Only available until 31/12/12 |
|  | 1517-1525 MHz | Individual license Details in Annex 27 | Maximum in-band ERP 20 dBW | technology neutral but typically used for: audio links | FS, MS, MSS | No |
|  | 5850-5925*, 7110-7250*, 7300-7425, 8460-8500, 12200-12500 MHz | Individual license Details in Annex 27 | Maximum in-band ERP 40 dBW (13 dBW airborne) cameras typically 1 W *Some airborne use permitted | technology neutral but typically used for: video links and wireless cameras | FS, MS, FSS, BSS, Space research | No |
| 28- RUS | 7750-7750 MHz | Light license Details in Annex 28 | transmit power – max 0 dBW (1W), antenna gain –max 35dB, not interfere to governmental propose equipment , not claim interference protection | Fixed and mobile ENG | FS, FSS | No |
|  | 8400-8700 MHz | Light license Details in Annex 28 | transmit power – max 0 dBW (1W), antenna gain –max 35dB, not interfere to governmental propose equipment , not claim interference protection | Fixed and mobile ENG | MS (except AMS), FS, Radiolocation, Space exploration | No |
|  | 12.75-13.25 GHz | Individual license Details in Annex 28 | transmit power – max 0 dBW (1W), detailed conditions could be defined in licence as result of expertize | mobile ENG | MS, FS, FSS(s-E), Space exploration | No |
| 29- IRL | 1980 – 2025 MHz 2170 – 2200 MHz | Individual license Details in Annex 29 | Max ERP: 5W Max Channel Bandwidth: 10 MHz. Airborne use is permitted only in 1980-2025 MHz. Details in Annex 29 | wireless cameras | 1980 – 2025 MHz: IMT-2000/UMTS Satellite Components, IMT-2000/UMTS Terrestrial 2170 - 2200 MHz: IMT-2000/UMTS terrestrial | No |
|  | 6.425 – 7.125 GHz 7.125 -7.425 GHz | Individual license Details in Annex 29 | Max ERP: 5W Max Channel Bandwidth: 10 or 20 MHz. wireless cameras for indoor events. Details in Annex 29 | wireless cameras | Fixed point-to-point radio links (Infrastructure), Fixed –Satellite (E/S) – VSATs, SRD’s, Fixed Satellite (E/S)(S/E), Meteorological Satellite (S/E). |  |
| 30- MLT | / | / | / | / | / | / |
| 31- E | None |  |  |  |  |  |
| 32- POR | / | / | / | / | / | / |
| 33- GRC | 5925–6425, 6425–7110, 7125–7250, 7300–7425 MHz | Individual License for temporary use Details in Annex 33 | Defined on case by case basis | Temporary P-P video links | Fixed Service | No |
| 34- LVA | None |  |  |  |  |  |

Preliminary analysis

The other bands introduced by the countries replying to the questionnaire show a high degree of diversity which reflects the specific national situations.

However, it is noted that the availability of frequency bands within the 6/8 GHz range is mentioned by 8 countries for fixed and/or mobile ENG/OB.

Further analysis is required on the information related to these other bands introduced by national administrations.

21 PMSE spectrum needs

| Annex - Country | PMSE spectrum needs / Alternative bands |
| --- | --- |
| 1- MNE | No need for alternative bands |
| 2-CYP | / |
| 3- LUX | Slight increase of spectrum demands expected in future but for the time being, the current overall situation in Luxembourg remains quite stable. Only in case of major uncommonly sport and music events (e.g. Tour de France), some peak demands could occur for PMSE. No other bands are currently foreseen in Luxembourg. |
| 4- MKD | / |
| 5- ISL | / |
| 6- FIN | Increasing demand for all kinds of PMSE applications and PMSE spectrum especially during special events. There will be a requirement to find alternative bands in higher frequencies if the present bands are allocated to other applications, for example LTE. |
| 7- DNK | / |
| 8- CZE | / |
| 9- SUI | 200 MHz of spectrum for professional cordless cameras (without private cordless cameras) at frequencies below 4 GHz (due to radio propagation conditions). A minimum channel bandwith of 10 MHz is required. |
| 10-GEO | / |
| 11- HOL | Users and usage groups indicate a yearly growth of ~10% in use of low power wireless audio links (wireless microphones). The possibilities for wireless microphones and wireless audio links in VHF and UHF TV-bands has been seriously reduced due to the introduction of T-DAB and DVB-T and the digital dividend. Together with growing quality demand (HD/3D audio+video), problems are expected during large events and around production studio’s. |
| 12-NOR | The industry has yet to indicate required spectrum for PMSE. There seem to be a need for more spectrums for wireless cameras at major events. In Norway the spectrum shortage during special events is usually overcome by trading spectrum from other licensees for the duration of the event. To facilitate this, cameras should have a wide tuning range. |
| 13- EST | New harmonized frequency bands for the future should be designated for PMSE equipment internationally. Need for alternative harmonized bands for PMSE. |
| 14- BLR | / |
| 15- TUR | PMSE spectrum need is not a continuous need but a temporary need. Sometimes, demand can reach the supply. Current spectrum is considered to be sufficient in the future. |
| 16- LTU | No clear demand for additional PMSE spectrum in the future. No need for alternative bands |
| 17- D | The future spectrum needs for PMSE applications depend on various factors: For some application scenarios the number of devices used in parallel at the same location might increase to some extent. However, the resulting potential increased demand for spectrum might be compensated in multiple cases if spectral efficiency is increased by potential future technological advances of the employed hardware. Additionally to this, possible novel features or changed parameters of the applications like an increased bandwidth for HD or 3D material for cordless cameras might be taken into account. The allocation of spectrum that can be used to fulfill the demand of PMSE applications depends on the evaluation of the factors stated in the previous section as well as developments of other radio applications and services and might be adapted accordingly. |
| 18- F | In a preliminary analysis, France considers that the frequency requirements for mobile video links during specific events where spectrum needs is high. This cannot be satisfied by the channel permanently identified at national level. Studies could be undertaken for identification of frequency bands and access and sharing conditions for mobile video links to meet frequency requirements for these specific events. |
| 19- HRV | No expected decrease for the PMSE spectrum needs. The usage of alternative bands depends on industry demands and further decisions on the digital dividend usage in Croatia |
| 20- SVK | / |
| 21- SRB | / |
| 22- I | For the time being no needs for alternative bands |
| 23- S | / |
| 24-HNG | Due to the spreading of Electronic Communication Networks (e.g. in 470-682 MHz) PMSE devices will be phased out from currently available bands. There is a demand to at least as much spectrum for PMSE purposes as there were. There is also a clear but limited need for frequencies dedicated for this special purpose where PMSE devices can operate with protection from other uses. |
| 25- AUT | More relevant than a additional spectrum seems a granted interference free spectrum and no further spectrum losses below 790 MHz. No need for alternative bands if some interior restrictions regarding the current availability of spectrum because of current licenses conditions in Austria could be solved, like the unlimited expire date of old licenses. |
| 26- BUL | / |
| 27- G | / |
| 28- RUS | / |
| 29- IRL | With regard to wireless cameras, we see that usage demand may exceed supply with migration from SD to HD technology. Within Ireland, the vast majority of event organisers request to operate in the 2 GHz band. If some of these bands (ex. the 2.3 GHz band, 2 GHz TDD band etc) are allocated for future broadband or other applications, then we may foresee shortage for assigning spectrum for wireless camera applications. With regard to demands of, for example, wireless audio applications, technology developments may lead to greater spectrum efficiency with, for instance, the employment of cognitive radio techniques, which may in turn lead to less overall spectrum usage requirements. ComReg believes that there is currently sufficient spectrum for PMSE activities within Ireland. On this basis, no alternative bands have yet been considered. That said, ComReg also understands that requirements for PMSE may change in the future, and therefore continuously monitors this domain for increased demand, application requirements, and technology developments which may lead to more efficient spectrum management. |
| 30- MLT | In Malta, all requests for PMSE spectrum have so far been accommodated. However, more spectrum bands need to be made available to certain applications such as radio microphones. |
| 31- E | The demand of the users will increase in the band 470-790 MHz for temporary events. |
| 32- POR | The demand of wireless cameras and video links is increasing, namely on a temporary basis for big events, and the frequency bands available are becoming scarce. Concerning potential alternative bands, the DAB L-band (1452-192 MHz) could be an alternative, as well as the unpaired 2 GHz bands (1900-1920 MHz / 2010-2025 MHz). |
| 33- GRC | There seems to be a need to accommodate wireless cameras, especially in the range below 3 GHz, that might not be able to be satisfied particularly for medium to large scale events. |
| 34- LVA | The need for alternative bands depends on industry demands. Alternative harmonized bands might be required. |

Preliminary analysis

21 countries gave their opinion regarding PMSE spectrum needs and potential alternative bands. The views expressed cover a wide range. There is a general feeling regarding a slight increase of spectrum demands. However, this does not necessarily mean that any additional or alternative band is required. Further consideration is required.