## Slide 1: Thomas Weilacher WG FM Chairman
1
CEPT Workshop on
Machine-To-Machine Communications (M2M)
Outcome; APs for ongoing activities
Mainz / Germany
21 – 22 March 2016

## Slide 2: Workshop on Machine-To-Machine Communications (M2M)
Key elements / action points for ongoing ECC activities:
Spectrum:
3GPP has defined solutions for M2M, i.e. EC-GSM-IoT, LTE-M and NB-IoT. In particular, NB-IoT (based on 200 kHz channel bandwidth) can be easily inserted in GSM, UMTS or LTE bands and can be considered as flexible when it comes to deployment and enables easy implementation. 3GPP Release 15 “pre-5G”, will include M2M solutions (target dates: June 2018, and Release 16 by end of 2019).

## Slide 3: Workshop on Machine-To-Machine Communications (M2M)
Key elements / action points for ongoing ECC activities:
Spectrum:
Harmonised spectrum for MFCN is already used for M2M communications. Will there be an impact on GSM switch off ???
M2M, 2 x 3 MHz in 700 MHz, has been studied by CEPT/ECC: ECC Report 242 (no further action on that).

## Slide 4: Workshop on Machine-To-Machine Communications (M2M)
Key elements / action points for ongoing ECC activities:
Spectrum:
The interest of dedicated spectrum for M2M networks for utilities in the band 450-470 MHz (and possibly in 410-430 MHz) was emphasised taking into account the propagation characteristics of these bands.
ECC/ WGFM should consider whether LTE studies (to be taken on-board in FM54/SE7) in this range could potentially also take into account on NB-IoT.

## Slide 5: Workshop on Machine-To-Machine Communications (M2M)
Key elements / action points for ongoing ECC activities:
Spectrum:
Forecasts expect the M2M traffic in wireless networks to quadruple within the 2015-2022 timeframe, carried over cellular networks as well as low power local and wide area networks. This will cause pressure on the current use in frequency bands, especially below 1 GHz. Spectrum usage below 1 GHz may be complemented in the future with higher frequency bands. Demand for unlicensed and individually licensed spectrum.

## Slide 6: Workshop on Machine-To-Machine Communications (M2M)
Key elements / action points for ongoing ECC activities:
Spectrum:
Individually licensed bands (MFCN, PMR, PAMR), de facto exclusive, suitable for specific M2M requirements. Commercial mobile broadband networks can also be used for mission critical purposes (smart grid) if conditions are met (hardened LTE networks, control over the network).

## Slide 7: Workshop on Machine-To-Machine Communications (M2M)
Key elements / action points for ongoing ECC activities:
Spectrum:
Solutions for short range / long range communication, including also meshed network, ad-hoc network solutions, and some very asymmetric network solutions where network relay points and individual sensors/actuators may need to be treated differently in frequency regulation.

## Slide 8: Workshop on Machine-To-Machine Communications (M2M)
Key elements / action points for ongoing ECC activities:
Spectrum:
Concerning unlicensed use, there was a strong request for more harmonisation in 870-876/915-921 MHz (seventh ETSI SRDoc on its way and a total of 10 presentations addressed this topic). CEPT announced that an Addendum to CEPT Report 59 (6th update of EC Decision on SRDs) is planned for the end of the year. For this, there is also the need to find a balance between national flexibility and the right level of EU harmonisation. Note also that some studies are on-going and changes in the future may occur for the regulations, e.g. introduction of more flexibility for the duty cycles. The 870-876 and 915-921MHz bands for SRDs, which is being underused in most European countries according to ECC Rep. 189, but designated for other radio applications (E-GSM-R, governmental applications).

## Slide 9: Workshop on Machine-To-Machine Communications (M2M)
Key elements / action points for ongoing ECC activities:
Spectrum:
In this respect, the suitability of duty cycle definitions for M2M was questioned taking into account that some devices may normally transmit at very LDC while having a need for higher DC when a specific event happen (emergency, alarm, tracking mode …).
Current regulatory frame conditions with regard to M2M, i.e. considering separately licensed and unlicensed bands were not questioned.

## Slide 10: Workshop on Machine-To-Machine Communications (M2M)
Key elements / action points for ongoing ECC activities:
Spectrum:
PMR solutions were described, notably in the 400 MHz band, in particular for mission-critical M2M applications and platforms, or where there is a need for a larger degree of customising the network to the needs of the M2M network provider.
Different models, dedicated and shared IoT networks, also hybrids, are possible, and may be driven by business case needs. This could also trigger the need to find synergies for common national platforms.

## Slide 11: Workshop on Machine-To-Machine Communications (M2M)
Key elements / action points for ongoing ECC activities:
Spectrum:
Appropriate authorisation/notification for shared spectrum access (especially in 400 MHz, 870-876/915-921 MHz) for achieving coexistence between M2M and the incumbent applications as well as between various M2M networks (see also ECC Report 132) may be an option and should further be considered.
Extra high voltage and high voltage smart grid will require enhanced communication and resilience systems.
Low voltage smart grid might be appropriate for licence exempted M2M spectrum.

## Slide 12: Workshop on Machine-To-Machine Communications (M2M)
Key elements / action points for ongoing ECC activities:
Spectrum:
Consideration of the requirements for Mesh-Networks (self-organisation, indoor/outdoor frequency agile systems). Spectrum requirements: 3 MHz (minimum).

## Slide 13: Workshop on Machine-To-Machine Communications (M2M)
Key elements / action points for ongoing ECC activities:
Spectrum:
Additionally, 5G spectrum will be considered under Agenda Item 1.13 of WRC-19 dealing with IMT2020 but spectrum options are above 24 GHz and technical conditions may not be suitable for many M2M applications (what is the contribution for Massive IoT and critical IOT ?).

## Slide 14: Workshop on Machine-To-Machine Communications (M2M)
Key elements / action points for ongoing ECC activities:
Spectrum:
There are several challenging needs for some of the M2M applications: massive deployments (up to several ten thousands of devices per km2 in metropolitan areas); but also in some cases, very high reliable and very low latency communications.

## Slide 15: Workshop on Machine-To-Machine Communications (M2M)
Key elements / action points for ongoing ECC activities:
Spectrum:
So far, some demand has been expressed for licence-exempt usage of the 1900-1920 MHz band (DECT community, some SRDs); ECC is ready to consider candidate applications for more efficient use of spectrum (see also draft CEPT Report 59).

## Slide 16: Workshop on Machine-To-Machine Communications (M2M)
Key elements / action points for ongoing ECC activities:
Spectrum:
Example Technologies (there are many more): cellular: EC-GSM-IoT, NB-IoT, LTE-M, 5G MTC; autonomous, licence-exempt: 802.11ah, BTLE, 802.15.4q, DECT); dedicated network: LTN, RPMA, WMbus, 802.15.4g.

## Slide 17: Workshop on Machine-To-Machine Communications (M2M)
Key elements / action points for ongoing ECC activities:
Spectrum:
Broad designation (technology neutral) to MFCN / ECN also enables M2M usage.
QoS to be considered .
Road safety related ITS: How could the interoperability / coexistence of different technologies be ensured (ITS-G5, LTE-V2X) in the band 5875-5905 MHz? Views from OEMs are also relevant. Hybrid solutions with vehicle sensor platforms will also play an important role in the future developments towards improved road-safety.
The potential interest in ITS in the range 5855-5875 MHz and 5905-5925 MHz is to be considered.

## Slide 18: Workshop on Machine-To-Machine Communications (M2M)
Key elements / action points for ongoing ECC activities:
Spectrum:
Interoperability between M2M devices should be achieved (non-proprietary standards).
Spectrum for Wireless Industrial Applications (WIA) in the range 1.4 GHz … 6 GHz (about 80 MHz, e.g. 2 x 40 MHz, required by the industry) may need some review, by taking into account global requirements. Band 1900-1920 MHz may be part of the discussion.

## Slide 19: Workshop on Machine-To-Machine Communications (M2M)
Key elements / action points for ongoing ECC activities:
Spectrum:
Additional ideas on national level (not already addressed above): UK: Further ideas for 55-68 MHz, 70.5-71.5 MHz and 80.0-81.5 MHz. RUS: Bands are under study (licensed / licence exempt usage). Question: What about satellite based solutions?

## Slide 20: Workshop on Machine-To-Machine Communications (M2M)
Key elements / action points for ongoing ECC activities:
Spectrum:
Additional ideas on national level (not already addressed above): France: Main targeted bands: 870-876 MHz, 915-921 MHz (but also new spectrum regulatory approach within 862-870 MHz); focus on 915-921 MHz (no national demand for E-GSM-R).

## Slide 21: Workshop on Machine-To-Machine Communications (M2M)
Key elements / action points for ongoing ECC activities:
Spectrum:
Additional ideas on national level (not already addressed above): D: Use of harmonised bands (look at the supply side). For new applications / bands: established ECC/ETSI process to be used. SWE: Most M2M applications can be carried over SRDs, RLANs, PMR or WBB (Wireless Broadband); general national strategy / management of spectrum demand (7 steps, for specific cases a faster process would be wishful).

## Slide 22: Workshop on Machine-To-Machine Communications (M2M)
Key elements / action points for ongoing ECC activities:
Numbering:
Not all M2M devices will require public numbering resources but the demand will still be significant.
Embedded smart card technology (eUICC (“eSIM”)) would seem to provide a solution to the “operator lock-in” issue as well as providing a platform for M2M device manufacturers to leverage economies of scale in the supply chain. A standardised approach is advisable and there are still some key questions to be resolved.

## Slide 23: Workshop on Machine-To-Machine Communications (M2M)
Key elements / action points for ongoing ECC activities:
Numbering:
Number portability does not seem to be relevant for M2M but the end-user right to retain use of a number when switching is clear in the Universal Services Directive. This requirement needs careful consideration in the forthcoming review of the framework to take account of the M2M market and might be revisited in order to encompass the switching of M2M connectivity provider.

## Slide 24: Workshop on Machine-To-Machine Communications (M2M)
Key elements / action points for ongoing ECC activities:
Numbering:
No special treatment of IoT services and/or M2M communication appears necessary at this time, except for certain areas where a clarification and/or a new approach might be appropriate (e.g. roaming, switching, number portability).
A consensus view was expressed by all panellists that a new European Numbering solution was not necessary.

## Slide 25: Workshop on Machine-To-Machine Communications (M2M)
Key elements / action points for ongoing ECC activities:
Numbering:
In the area of numbering there may be a scope for considering the creation of a light-touch Pan-EU Authorisation/Notification for M2M/IoT to reflect customer demand and facilitate pan-EU service provision.

## Slide 26: Workshop on Machine-To-Machine Communications (M2M)
Key elements / action points for ongoing ECC activities:
Numbering:
Extra-territorial use of E.164 numbers is an inevitable evolution particularly in an M2M market that is inherently global. Use of national numbers and international ITU-numbers should be considered as complementary options for the provision of global M2M services without being promoted, imposed or prevented by regulation. Some of the challenges with international resources could be investigated further. However, transparency regarding the extra-territorial use of national numbers needs to be promoted, without putting disproportionate burdens on the M2M market.

## Slide 27: Workshop on Machine-To-Machine Communications (M2M)
Thank you very much